## Slide 1: COMP 122/L Lecture 2 Mahdi Ebrahimi Slides adapted from Dr. Kyle Dewey

## Slide 2: Outline
Operations on binary values
  AND, OR, XOR, NOT
  Bit shifting (left, two forms of right)
  Addition
  Subtraction
Twos complement

## Slide 3: Bitwise Operations

## Slide 4: Bitwise AND
Similar to logical AND (&&), except it works on a bit-by-bit manner
Denoted by a single ampersand: &
(1001 &
0101)=
0001

## Slide 5: Bitwise OR
Similar to logical OR (||), except it works on a bit-by-bit manner
Denoted by a single pipe character: |
(1001 |
0101)=
1101

## Slide 6: Bitwise XOR
Exclusive OR, denoted by a carat: ^
Similar to bitwise OR, except that if both inputs are 1 then the result is 0
(1001 ^
0101)=
1100

## Slide 7: Bitwise NOT
Similar to logical NOT (!), except it works on a bit-by-bit manner
Denoted by a tilde character: ~
~1001 = 0110

## Slide 8: Shift Left
Move all the bits N positions to the left, subbing in N 0s on the right

## Slide 9: Shift Left
Move all the bits N positions to the left, subbing in N 0s on the right
1001

## Slide 10: Shift Left
Move all the bits N positions to the left, subbing in N 0s on the right
1001 << 2 =
100100

## Slide 11: Shift Left
Useful as a restricted form of multiplication
Question: how?
1001 << 2 =
100100

## Slide 12: Shift Left as Multiplication
Equivalent decimal operation:
234

## Slide 13: Shift Left as Multiplication
Equivalent decimal operation:
234 << 1 =
2340

## Slide 14: Shift Left as Multiplication
Equivalent decimal operation:
234 << 1 =
2340
234 << 2 =
23400

## Slide 15: Multiplication
Shifting left N positions multiplies by
(base)N
Multiplying by 2 or 4 is often necessary (shift left 1 or 2 positions, respectively)
Often a whooole lot faster than telling the processor to multiply
Compilers try hard to do this
234 << 2 =
23400

## Slide 16: Shift Right
Move all the bits N positions to the right, subbing in either N 0s or N 1s on the left
  Two different forms

## Slide 17: Shift Right
Move all the bits N positions to the right, subbing in either N 0s or N (whatever the leftmost bit is)s on the left
  Two different forms
1001 >> 2 =
either 0010 or 1110

## Slide 18: Shift Right Trick
Question: If shifting left multiplies, what does shift right do?

## Slide 19: Shift Right Trick
Question: If shifting left multiplies, what does shift right do?
  Answer: divides in a similar way, but truncates result

## Slide 20: Shift Right Trick
Question: If shifting left multiplies, what does shift right do?
  Answer: divides in a similar way, but truncates result
234

## Slide 21: Shift Right Trick
Question: If shifting left multiplies, what does shift right do?
  Answer: divides in a similar way, but
truncates result
234 >> 1 =
23

## Slide 22: Two Forms of Shift Right
Subbing in 0s makes sense
What about subbing in the leftmost bit?
  And why is this called “arithmetic” shift right?
1100 (arithmetic)>> 1 =
1110

## Slide 23: Answer...Sort of
Arithmetic form is intended for numbers in two's complement, whereas the non- arithmetic form is intended for unsigned numbers

## Slide 24: Twos Complement

## Slide 25: Problem
Binary representation so far makes it easy to represent positive numbers and zero
Question:What about representing negative numbers?

## Slide 26: Twos Complement
Way to represent positive integers, negative integers, and zero
If 1 is in the most significant bit (generally leftmost bit in this class), then it is negative

## Slide 27: Decimal to Twos Complement
Example: -5 decimal to binary (twos complement)

## Slide 28: Decimal to Twos Complement
Example: -5 decimal to binary (twos complement)
First, convert the magnitude to an unsigned representation

## Slide 29: Decimal to Twos Complement
Example: -5 decimal to binary (twos complement)
First, convert the magnitude to an unsigned representation
5 (decimal) = 0101 (binary)

## Slide 30: Decimal to Twos Complement
Then, take the bits, and negate them

## Slide 31: Decimal to Twos Complement
Then, take the bits, and negate them
0101

## Slide 32: Decimal to Twos Complement
Then, take the bits, and negate them
~0101 = 1010

## Slide 33: Decimal to Twos Complement
Finally, add one:

## Slide 34: Decimal to Twos Complement
Finally, add one:
1010

## Slide 35: Decimal to Twos Complement
Finally, add one:
1010 + 1 =
1011

## Slide 36: Twos Complement to Decimal
Same operation: negate the bits, and add one

## Slide 37: Twos Complement to Decimal
Same operation: negate the bits, and add one
1011

## Slide 38: Twos Complement to Decimal
Same operation: negate the bits, and add one
~1011 = 0100

## Slide 39: Twos Complement to Decimal
Same operation: negate the bits, and add one
0100

## Slide 40: Twos Complement to Decimal
Same operation: negate the bits, and add one
0100 + 1 =
0101

## Slide 41: Twos Complement to Decimal
Same operation: negate the bits, and add one
0100 + 1 =
0101 =
-5
We started with
1011 - negative

## Slide 42: Intuition
Modular arithmetic, with the convention that a leading 1 bit means negative
000
001
010
011
100
101
110
111
Denotes
+1
Notes: -This is the intuition from Wikipedia, which makes a whole lot more sense

## Slide 43: Intuition
Modular arithmetic, with the convention that a
000
100
101
Denotes
+1
(least -) 111 001 (least +)
110 010
011 (most +) (most -)
leading 1 bit means negative
(zero)
Notes: -This is the intuition from Wikipedia, which makes a whole lot more sense
-There is still a lot of detail missing here - it’s not necessary to understand in order to work with this.
There is actually quite a bit of mathematics behind why this works

## Slide 44: Intuition
Modular arithmetic, with the convention that a
000
Denotes
+1
leading 1 bit means negative
0
001 1
010 2
011 3
100
-4
-3 101
-2 110
-1 111
Notes: -This is the intuition from Wikipedia, which makes a whole lot more sense
-There is still a lot of detail missing here - it’s not necessary to understand in order to work with this.
There is actually quite a bit of mathematics behind why this works

## Slide 45: Negation of 1
000
001
010
011
100
101
110
111
Notes: -Take our wheel from before

## Slide 46: Negation of 1
000
001
010
011
100
101
110
111
Notes: -This is 1

## Slide 47: Negation of 1
000
001
010
011
100
101
110
111
Notes: -Inverted bits

## Slide 48: Negation of 1
000
001
010
011
100
101
110
111
Notes: -Add 1
-This is exactly what we expected - binary 111 represents decimal -1

## Slide 49: Consequences
What is the negation of 000?
000
111 001
110 010
101 011
100
Notes: -Negate all bits: 000 -> 111
-Add one: 000
-Technically, adding one resulted in 1000, but that got cut off

## Slide 50: Consequences
What is the negation of 100?
000
111 001
110 010
101 011
100
Notes: -Negate all bits: 100 -> 011
-Add one: 100
-Uh oh...this states that the negation of -4 is -4.
-Underlying problem is that we don’t have a representation for 4 with just three bits

## Slide 51: Arithmetic Shift Right
Not exactly division by a power of two
Consider -3 / 2
0
000
001 1
010 2
011 3
100
-4
-2 110
-3 101
-1 111
Notes: -101 (-3) shifted right yields 110 (-2), NOT 111 (-1) as expected from typical integer division
-Integer division rounds towards zero, whereas shift right rounds towards negative infinity
-This means they work _identically_ for positive values, but not for negative values (also meaning they are always the same for _unsigned_ values)

## Slide 52: Addition
http://sandbox.mc.edu/~bennet/cs110/textbook/module3_2.html

## Slide 53: Building Up Addition
Question: how might we add the following, in decimal?
986
+123
----
?

## Slide 54: Building Up Addition
Question: how might we add the following, in decimal?
986
+123
----
?
6
+3
--
?

## Slide 55: Building Up Addition
Question: how might we add the following, in decimal?
986
+123
----
?
6
+3
--
9
8
+2
--
?

## Slide 56: Building Up Addition
Question: how might we add the following, in decimal?
986
+123
----
?
6
+3
--
9
8
+2
--
0
Carry: 1

## Slide 57: Building Up Addition
Question: how might we add the following, in decimal?
986
+123
----
?
6
+3
--
9
8
+2
--
0
1
9
+1
--
?

## Slide 58: Building Up Addition
Question: how might we add the following, in decimal?
986
+123
----
?
6
+3
--
9
8
+2
--
0
1
9
+1
--
1
Carry: 1

## Slide 59: Building Up Addition
Question: how might we add the following, in decimal?
986
+123
----
?
6
+3
--
9
8
+2
--
0
1
9
+1
--
1
1
+0
--
1

## Slide 60: Core Concepts
We have a “primitive” notion of adding single digits, along with an idea of carrying digits
We can build on this notion to add numbers together that are more than one digit long

## Slide 61: Now in Binary
Arguably simpler - fewer one-bit possibilities
0 | 0 | 1 | 1
+0 | +1 | +0 | +1
-- | -- | -- | --
? | ? | ? | ?

## Slide 62: Now in Binary
Arguably simpler - fewer one-bit possibilities
0 | 0 | 1 | 1
+0 | +1 | +0 | +1
-- | -- | -- | --
0 | 1 | 1 | 0
Carry: 1

## Slide 63: Chaining the Carry
Also need to account for any input carry
0 | 0 | 0 | 0
0 | 0 | 1 | 1
+0 -- | +1 -- | +0 -- | +1 --
0 | 1 | 1 | 0 Carry:
1 | 1 | 1 | 1
0 | 0 | 1 | 1
+0 | +1 | +0 | +1
-- | -- | -- | --
1 | 0 Carry: 1 0 Car |  | ry: 1 1 Carry: 1
1

## Slide 64: Adding Multiple Bits
How might we add the numbers below?
011
+001
------

## Slide 65: Adding Multiple Bits
How might we add the numbers below?
0
011
+001
------
Notes: -Need an initial carry-in of zero

## Slide 66: Adding Multiple Bits
------
0
How might we add the numbers below?
10
011
+001
Notes: -Need an initial carry-in of zero

## Slide 67: Adding Multiple Bits
------
00
How might we add the numbers below?
110
011
+001
Notes: -Need an initial carry-in of zero

## Slide 68: Adding Multiple Bits
------
100
How might we add the numbers below?
0110
011
+001
Notes: -Need an initial carry-in of zero

## Slide 69: Adding Multiple Bits
------
100
How might we add the numbers below?
0110
011
+001
Output Carry Bit
Result Bits
Notes: -Need an initial carry-in of zero

## Slide 70: Another Example
111
+001
------

## Slide 71: Another Example
0
111
+001
------

## Slide 72: Another Example
------
0
10
111
+001

## Slide 73: Another Example
------
00
110
111
+001

## Slide 74: Another Example
------
000
1110
111
+001
Output Carry Bit
Result Bits
Notes: -Now we have an output carry bit of 1.
What does this mean?

## Slide 75: Output Carry Bit Significance
For unsigned numbers, it indicates if the result did not fit all the way into the number of bits allotted
May be an error condition for software

## Slide 76: Signed Addition
Question: what is the result of the following operation?
011
+011
----
?

## Slide 77: Signed Addition
Question: what is the result of the following operation?
011
+011
---- 0110
Notes: -If these are treated as signed numbers in two’s complement, then we need a leading 0 to indicate that this is a positive number
-Truncated to three bits, the result is a negative number!

## Slide 78: Overflow
In this situation, overflow occurred: this means that both the operands had the same sign, and the result’s sign differed
011
+011
---- 110
Possibly a software error

## Slide 79: Overflow vs. Carry
These are different ideas
  Carry is relevant to unsigned values
  Overflow is relevant to signed values
Overflow; No Carry
No Overflow; Carry
Overflow; Carry
111 | 011 | 111 | 001
+001 | +011 | +100 | +001
---- | ---- | ---- | ----
000 | 110 | 011 | 010
No Overflow; No Carry
Notes: -As to when is it a problem, this all depends on exactly what it is you’re doing

## Slide 80: Subtraction

## Slide 81: Subtraction
Have been saying to invert bits and add one to second operand
Could do it this way in hardware, but there is a trick
001
-001
----
?
001
+111
----
?
Hint: these two questions are equivalent

## Slide 82: Subtraction Trick
Assume we can cheaply invert bits, but we want to avoid adding twice (once to add 1 and once to add the other result)
How can we do this easily?

## Slide 83: Subtraction Trick
Assume we can cheaply invert bits, but we want to avoid adding twice (once to add 1 and once to add the other result)
How can we do this easily?
  Set the initial carry to 1 instead of 0

## Slide 84: Subtraction Example
0101
-0011
----

## Slide 85: Subtraction Example
0101
-0011
----
Invert 0011

## Slide 86: Subtraction Example
0101
-0011
----
Invert 0011
1100

## Slide 87: Subtraction Example
0101
-0011
----
Invert 0011
1100
Equivalent to

## Slide 88: Subtraction Example
0101
-0011
----
Invert 0011
1100
Equivalent to
1
0101
+1100
----
Notes: -An initial carry-in of 1 is equivalent to adding 1 and then adding the other operand

## Slide 89: Subtraction Example
0101
-0011
----
Invert 0011
1100
Equivalent to
+1100
----
0010
11011
0101
Notes: -An initial carry-in of 1 is equivalent to adding 1 and then adding the other operand