## Slide 1: Number Systems
So far we have studied the following integer number systems in computer
  Unsigned numbers
  Sign/magnitude numbers
  Two’s complement numbers
What about rational numbers?
  For example, 2.5, -10.04, 0.75 etc
Two common notations to represent rational numbers in computer
  Fixed-point numbers
  Floating-point numbers

## Slide 2: Fixed-Point Numbers
Fixed point notation has an implied binary point between the integer and fraction bits
  The binary point is not a part of the representation but is implied
  Example:
    Fixed-point representation of 6.75 using 4 integer bits and 4 fraction bits:
The number of integer and fraction bits must be agreed upon by those generating and those reading the number
  There is no way of knowing the existence of the binary point except through agreement of those people interpreting the number

## Slide 3: Signed Fixed-Point Numbers
As with whole numbers, negative fractional numbers can be represented in two ways
  Sign/magnitude notation
  Two’s complement notation
Example:
  -2.375 using 8 bits (4 bits each to represent integer and fractional parts)
    2.375 = 0010 . 0110
    Sign/magnitude notation: 1010 0110
    Two’s complement notation:
  1. flip all the bits: 1101 1001
  2. add 1: + 1
  1101 1010
Addition and subtraction works easily in computer with 2’s complement notation like integer addition and subtraction

## Slide 4: Example
Suppose that we have 8 bits to represent a number
  4 bits for integer and 4 bits for fraction
Compute 0.75 + (-0.625)
  0.75 = 0000 1100
  0.625 = 0000 1010
  -0.625 in 2’s complement form: 1111 0110
  0.75 0000 1100
  + - 0.625 1111 0110
  0000 0010
0.125

## Slide 5: Fixed-Point Number Systems
Fixed-point number systems have a limitation of having a constant number of integer and fractional bits
  What are the largest and the smallest rational numbers you can represent with 32 bits, assuming 16 bits each for integer and fractional parts?
Some low-end digital signal processors support fixed-point numbers
  Example: TMS320C550x TI (Texas Instruments) DSPs: www.ti.com

## Slide 6: Floating-Point Numbers
Floating-point number systems circumvent the limitation of having a constant number of integer and fractional bits
  They allow the representation of very large and very small numbers
The binary point floats to the right of the most significant 1
  Similar to decimal scientific notation
  For example, write 27310 in scientific notation:
    Move the decimal point to the right of the most significant digit and increase the exponent:
  273 = 2.73 × 102
In general, a number is written in scientific notation as:
± M × BE
Where,
  M = mantissa
  B = base
  E = exponent
  In the example, M = 2.73, B = 10, and E = 2 (that is, +2.73 × 102)

## Slide 7: Floating-Point Numbers
Floating-point number representation using 32 bits
  1 sign bit
  8 exponent bits
  23 bits for the mantissa.
The following slides show three versions of floating-point representation with 22810 using a 32-bit
  The final version is called the IEEE 754 floating-point standard

## Slide 8: Floating-Point Representation #1
First, convert the decimal number to binary
  22810 = 111001002 = 1.11001 × 27
Next, fill in each field in the 32-bit:
  The sign bit (1 bit) is positive, so 0
  The exponent (8 bits) is 7 (111)
  The mantissa (23 bits) is 1.11001

## Slide 9: Floating-Point Representation #2
You may have noticed that the first bit of the mantissa is always 1, since the binary point floats to the right of the most significant 1
  Example: 22810 = 111001002 = 1.11001 × 27
Thus, storing the most significant 1 (also called the implicit leading 1) is redundant information
We can store just the fraction parts in the 23-bit field
  Now, the leading 1 is implied
0 0 0 0 0 1 1 1

## Slide 10: Floating-Point Representation #3
  The exponent needs to represent both positive and negative
The final change is to use a biased exponent
  The IEEE 754 standard uses a bias of 127
  Biased exponent = bias + exponent
    For example, an exponent of 7 is stored as 127 + 7 = 134 = 100001102
Thus , 22810 using the IEEE 754 32-bit floating-point standard is

## Slide 11: Example
Represent -5810 using the IEEE 754 floating-point standard
  First, convert the decimal number to binary
    5810 = 1110102 = 1.1101 × 25
  Next, fill in each field in the 32-bit number
    The sign bit is negative (1)
    The 8 exponent bits are (127 + 5) = 132 = 10000100(2)
    The remaining 23 bits are the fraction bits: 11010000..000(2)
  It is 0xC2680000 in the hexadecimal form
    Check this out with the result of the sample program in the slide# 3

## Slide 12: Floating-Point Numbers: Special Cases
The IEEE 754 standard includes special cases for numbers that are difficult to represent, such as 0 because it lacks an implicit leading 1
Number | Sign | Exponent | Fraction
0 | X | 00000000 | 00000000000000000000000
∞ | 0 | 11111111 | 00000000000000000000000
- ∞ | 1 | 11111111 | 00000000000000000000000
NaN | X | 11111111 | non-zero
  NaN is used for numbers that don’t exist, such as √-1 or log(-5)

## Slide 13: Floating-Point Number Precision
The IEEE 754 standard also defines 64-bit double-precision that provides greater precision and greater range
  Single-Precision (use the float declaration in C language)
    32-bit notation
    1 sign bit, 8 exponent bits, 23 fraction bits
    bias = 127
    It spans a range from ±1.175494 X 10-38 to ±3.402824 X 1038
  Double-Precision (use the double declaration in C language)
    64-bit notation
    1 sign bit, 11 exponent bits, 52 fraction bits
    bias = 1023
    It spans a range from ±2.22507385850720 X 10-308 to ±1.79769313486232 X 10308
Most general purpose processors (including Intel and AMD processors) provide hardware support for double-precision floating-point numbers and operations

## Slide 14: Double Precision Example
Represent -5810 using the IEEE 754 double precision
  First, convert the decimal number to binary
    5810 = 1110102 = 1.1101 × 25
  Next, fill in each field in the 64-bit number
    The sign bit is negative (1)
    The 11 exponent bits are (1023 + 5) = 1028 = 10000000100(2)
    The remaining 52 bits are the fraction bits: 11010000..000(2)
  It is 0xC04D0000_00000000 in the hexadecimal form
    Check this out with the result of the sample program in the slide# 4

## Slide 15: Represent 0.7
Represent 0.7 in IEEE 754 single precision form
  ½ = 0.5 = 0.1(2) // 0.7-0.5 = 0.2
  1/8 = 0.125 = 0.001(2) // 0.2-0.125=0.075
  1/16 = 0.0625 = 0.0001(2) // 0.075-0.0625=0.0125
  1/128 = 0.0078125 = 0.0000001(2) // 0.0125-0.0078125 =0.0046875
  1/256 = 0.00390625 = 0.00000001(2) // 0.0046875-0.00390625=0.00078125
  ……
  Thus, 0.7 = 0.10110011…(2) = 1.0110011…(2) X 2-1
    In IEEE754 single precision, 0.7 = 0x3F333333
    Check it out with the slide#6
IEEE754 floating-point standard can’t represent some numbers exactly

## Slide 16: Binary Coded Decimal (BCD)
Since floating-point number systems can’t represent some numbers exactly such as 0.1 and 0.7, some application (calculators) use BCD (Binary coded decimal)
  BCD numbers encode each decimal digit using 4 bits with a range of 0 to 9
  BCD fixed-point notation examples
    1.7 = 0001 . 0111
    4.9 = 0100 . 1001
BCD is very common in electronic systems where a numeric value is to be displayed, especially, in systems consisting solely of digital logic (not containing a microprocessor) - Wiki
Decimal | BCD Digit
0 | 0000
1 | 0001
2 | 0010
3 | 0011
4 | 0100
5 | 0101
6 | 0110
7 | 0111
8 | 1000
9 | 1001

## Slide 17
Backup Slides

## Slide 18: Floating-Point Numbers: Rounding
Arithmetic results that fall outside of the available precision must round to a neighboring number
Rounding modes
  Round down
  Round up
  Round toward zero
  Round to nearest
Example
  Round 1.100101 (1.578125) so that it uses only 3 fraction bits
    Round down: 1.100
    Round up: 1.101
    Round toward zero: 1.100
    Round to nearest: 1.101
      1.625 is closer to 1.578125 than 1.5 is

## Slide 19: Floating-Point Addition with the Same Sign
Addition with floating-point numbers is not as simple as addition with 2’s complement numbers
The steps for adding floating-point numbers with the same sign are as follows
  Extract exponent and fraction bits
  Prepend leading 1 to form mantissa
  Compare exponents
  Shift smaller mantissa if necessary
  Add mantissas
  Normalize mantissa and adjust exponent if necessary
  Round result
  Assemble exponent and fraction back into floating-point format

## Slide 20: Floating-Point Addition Example
Add the following floating-point numbers:
1.5 + 3.25
1.5(10) = 1.1(2) x 20
3.25(10) = 11.01(2) = 1.101(2) x 21
1.1(10) = 0x3FC00000 in IEEE 754 single precision
3.25(10) = 0x40500000 in IEEE 754 single precision

## Slide 21: Floating-Point Addition Example
1. Extract exponent and fraction bits
For first number (N1): S = 0, E = 127, F = .1
For second number (N2): S = 0, E = 128, F = .101
2. Prepend leading 1 to form mantissa
N1: 1.1
N2: 1.101

## Slide 22: Floating-Point Addition Example
3. Compare exponents
127 – 128 = -1, so shift N1 right by 1 bit
4. Shift smaller mantissa if necessary
shift N1’s mantissa: 1.1 >> 1 = 0.11 (× 21)
5. Add mantissas
0.11 × 21
+ 1.101 × 21
10.011 × 21

## Slide 23: Floating-Point Addition Example
6. Normalize mantissa and adjust exponent if necessary
10.011 × 21 = 1.0011 × 22
7. Round result
No need (fits in 23 bits)
8. Assemble exponent and fraction back into floating-point format
S = 0, E = 2 + 127 = 129 = 100000012, F = 001100..
4.75(10) = 0x40980000 in the hexadecimal form