## Slide 1: Lecture 7 Overview
1
Boolean Algebra
Standard or Canonical forms
Minterms/Maxterms
Karnaugh maps

## Slide 2: Combinational Logic Circuits
Logic gates combine several logic-variable inputs to produce a logic- variable output.
Combinational logic circuits are “memoryless” because their output value at a given instant depends only on the input values at that instant.
Sequential logic circuits possess memory because their present output value depends on previous as well as present input values.
2

## Slide 3: Terminology
A literal is a variable or its complement, e.g. X, X‘ or X
An expression consists of literals combined with AND, OR parentheses, complementation.
  X+Y
  P Q R
  A + B C
If in doubt about the meaning of an expression, make liberal use of parentheses.
An equation consists of the form: Variable = Expression.
P  ((X  Y ))  A B
3

## Slide 4: Simplifying Logic Functions (Logic Synthesis)
4
Logic Synthesis: reduce complexity of the gate level implementation
reduce number of literals (gate inputs)
reduce number of levels of gates
fewer inputs implies faster gates in some technologies
fan-ins (number of gate inputs) are limited in some technologies
fewer levels of gates implies reduced signal propagation delays

## Slide 5: Boolean Algebra
5
Switching algebra - deals with Boolean values - 0,1
Positive logic convention - LOW, HIGH - 0,1
Negative logic seldom used.
Signal values denoted by X,Y, A, B, C...

## Slide 6: Boolean Operators (Truth table)
OR X + Y
6
AND X . Y
Complement (opposite) X’

## Slide 7: Method I: Boolean Algebra
A  A  1
A  A
AND:
A 1  A
A  0  0 A  A  A
A  A  0
OR:
A  0  A A 1  1
NOT:
Associative Law:
(A·B)·C A·(B·C) A·B·C
(A  B)  C  A  (B  C)  A  B  C
Distributive Law:
A·(B C)  (A·B) (A·C)
A  (B·C)  (A  B) ·(A  C)
DeMorgan's Theorem:
(A·B) A  B (NAND) (A  B)  A· B (NOR)
7
A  A  A Idempotent Law:
Involution Law:
Identity Law:
Laws of Complementarity:
Commutative Law:
A·B B·A
A  B  B  A
Precedence:
AB  A·B
A·B C  (A·B) C A  B·C A  (B·C)
Absorption Law: A  A.B  A A.(A  B)  A

## Slide 8: Boolean Algebra
8
Duality: a dual of a Boolean expression is derived by replacing AND operations by ORs, OR operations by ANDs, constant 0s by 1s, and 1s by 0s (literals are left unchanged).
Any statement that is true for an expression is also true for its dual!
A . (B  C )  ( A . B )  ( A . C )
A  ( B . C )  ( A  B ) . ( A  C )

## Slide 9: Proving Theorems via Boolean Algebra
9
Proving theorems via axioms of Boolean Algebra:
prove the theorem: X • Y + X • Y' = X
distributive law X • Y + X •Y' = X • (Y + Y')
complementary law X • (Y + Y') = X • (1)
identity X • (1) = X
prove the theorem: X + X • Y = X
X + X • Y = X • 1 + X • Y
X • 1 + X • Y = X • (1 + Y)
X • (1 + Y)
X • (1)
= X • (1)
= X
Identity
distributive law
identity
identity

## Slide 10: Using the Rules of Boolean Algebra
Example: Simplify the following function:
Use X  X  1
Use X  YZ  (X  Y)  (X  Z) and X  X  1
=1
expand this

## Slide 11: SOP and POS
DeMorgan's Theorem shows that any logic function can be implemented by using just OR and NOT gates , or by just AND and NOT gates
A consequence of this is that any logical expression can be reduced to either a "Sum-of-Products (SOP)" form or a "Product-of-Sums (POS)" form
DeMorgan's Theorem:
(A·B)  A  B (NAND)
(A  B)  A · B (NOR)
THE DUAL IDEA

## Slide 12: SUM OF PRODUCTS (SOP)
“0th” level
We can write expressions in many ways, but some ways are more useful than others
A sum of products (SOP) expression contains:
  Only OR (sum) operations at the “outermost” level
  Each term that is summed must be a product of literals
f(x,y,z) = y’ + x’yz’ + xz
The advantage is that any sum of products expression can be implemented using a two-level circuit
  literals and their complements at the
  AND gates at the first level
  a single OR gate at the second level

## Slide 13: MINTERMS
Minterm Is true when… Shorthand x’y’z’ x=0, y=0, z=0 m0 x’y’z x=0, y=0, z=1 m1 x’yz’ x=0, y=1, z=0 m2 x’yz x=0, y=1, z=1 m3 xy’z’ x=1, y=0, z=0 m4 xy’z x=1, y=0, z=1 m5 xyz’ x=1, y=1, z=0 m6 xyz x=1, y=1, z=1 m7 | x | y | z | minterms | 
 | 0 | 0 | 0 | m0 | 
 | 0 | 0 | 1 | m2 | 
 | 0 | 1 | 0 | m2 | 
 | 0 | 1 | 1 | m3 | 
 | 1 | 0 | 0 | m4 | 
 | 1 | 0 | 1 | m5 | 
 | 1 | 1 | 0 | m6 | 
 | 1 | 1 | 1 | m7 | 
A minterm is a special product of literals, in which each input variable appears exactly once.
A function with n variables has 2n minterms (since each variable can appear complemented or not)
A three-variable function, such as f(x,y,z), has 23 = 8 minterms:
Each minterm is true for exactly one combination of inputs:
x’y’z’ xy’z’
x’y’z xy’z
x’yz’ xyz’
x’yz xyz

## Slide 14: SUM OF MINTERMS FORM
x | y | z | f(x,y,z) | f’(x,y,z)
0 | 0 | 0 | 1 | 0
0 | 0 | 1 | 1 | 0
0 | 1 | 0 | 1 | 0
0 | 1 | 1 | 1 | 0
1 | 0 | 0 | 0 | 1
1 | 0 | 1 | 0 | 1
1 | 1 | 0 | 1 | 0
1 | 1 | 1 | 0 | 1
Every function can be written as a sum of minterms, which is a special kind of sum of products form
The sum of minterms form for any function is unique
If you have a truth table for a function, you can write a sum of minterms expression just by picking out the rows of the table where the function output is 1.
f = x’y’z’ + x’y’z + x’yz’ + x’yz + xyz’
= m0 + m1 + m2 + m3 + m6
= m(0,1,2,3,6)
f’ = xy’z’ + xy’z + xyz
= m + m + m
4 5 7
= m(4,5,7)
f’ contains all the minterms not in f

## Slide 15: PRODUCTS OF SUMS (POS)
A product of sums (POS) expression contains:
  Only AND (product) operations at the “outermost” level
  Each term must be a sum of literals
f(x,y,z) = y’ (x’ + y + z’) (x + z)
Product of sums expressions can be implemented with two-level circuits
  literals and their complements at the “0th” level
  OR gates at the first level
  a single AND gate at the second level
Compare this with sums of products

## Slide 16: MAXTERMS
A maxterm is a sum of literals, in which each input variable appears exactly once.
A function with n variables has 2n maxterms
The maxterms for a three-variable function f(x,y,z):
Each maxterm is false for exactly one combination of inputs:
x’ + y’ + z’ | x’ + y’ + z | x’ + y + z’ | x’+ y + z
x + y’ + z’ | x + y’ + z | x + y + z’ | x + y + z
Maxterm | Is false when… | Shorthand
x + y + z | x=0, y=0, z=0 | M0
x + y + z’ | x=0, y=0, z=1 | M1
x + y’ + z | x=0, y=1, z=0 | M2
x + y’ + z’ | x=0, y=1, z=1 | M3
x’ + y + z | x=1, y=0, z=0 | M4
x’ + y + z’ | x=1, y=0, z=1 | M5
x’ + y’ + z | x=1, y=1, z=0 | M6
x’ + y’ + z’ | x=1, y=1, z=1 | M7

## Slide 17: PRODUCT OF MAXTERMS FORM
Every function can be written as a unique product of maxterms
If you have a truth table for a function, you can write a product of maxterms expression by picking out the rows of the table where the function output is 0. (Be careful if you’re writing the actual
literals!)
f’ contains all the maxterms not in f
x | y | z | f(x,y,z) | f’(x,y,z)
0 | 0 | 0 | 1 | 0
0 | 0 | 1 | 1 | 0
0 | 1 | 0 | 1 | 0
0 | 1 | 1 | 1 | 0
1 | 0 | 0 | 0 | 1
1 | 0 | 1 | 0 | 1
1 | 1 | 0 | 1 | 0
1 | 1 | 1 | 0 | 1
f = (x’ + y + z)(x’ + y + z’)(x’ + y’ + z’)
= M4 M5 M7
= ΠM(4,5,7)
f’ = (x + y + z)(x + y + z’)(x + y’ + z)
(x + y’ + z’)(x’ + y’ + z)
= M0 M1 M2 M3 M6
= ΠM(0,1,2,3,6)
in input column implies true literal
in input column implies complemented literal

## Slide 18: MINTERMS AND MAXTERMS ARE RELATED
Any minterm mi is the complement of the corresponding maxterm Mi
For example, m4’ = M4 because (xy’z’)’ = x’ + y + z
Minterm | Shorthand | Maxterm | Shorthand
x’y’z’ | m0 | x + y + z | M0
x’y’z | m1 | x + y + z’ | M1
x’yz’ | m2 | x + y’ + z | M2
x’yz | m3 | x + y’ + z’ | M3
xy’z’ | m4 | x’ + y + z | M4
xy’z | m5 | x’ + y + z’ | M5
xyz’ | m6 | x’ + y’ + z | M6
x’ + y’ + z’
M7
xyz
m7

## Slide 19: CONVERTING BETWEEN STANDARD FORMS
We can convert a sum of minterms to a product of maxterms
From before | f | = m(0,1,2,3,6) | 
and | f’ | = m(4,5,7) | 
 |  | = m4 + m5 + m7 | 
complementing (f’)’ = (m4 + m5 + m7)’ |  |  | 
so | f | = m4’ m5’ m7’ | [ DeMorgan’s law ]
 |  | = M4 M5 M7 | [ By the previous page ]
= ΠM(4,5,7)
In general, just replace the minterms with maxterms, using maxterm numbers that don’t appear in the sum of minterms:
f = m(0,1,2,3,6)
= ΠM(4,5,7)
The same thing works for converting from a product of maxterms to a sum of minterms

## Slide 20: Method II: Karnaugh Maps
A simpler way to handle most (but not all) jobs of manipulating logic functions.

## Slide 21: Karnaugh Map Advantages
Minimization can be done more systematically
Much simpler to find minimum solutions
Easier to see what is happening (graphical)
Almost always used instead of boolean minimization.

## Slide 22: Gray Codes
2-bit Gray Code
00
01
11
10
Gray code is a binary value encoding in which adjacent values only differ by one bit
Gray Codes
  To generate a gray code for n+1 bits, write down the gray code sequence for n bits
  Form one sequence with a prepended '0' to all the code words
  Form another sequence with a prepended '1' to all the code words
  Write the latter in reverse order.
  Concatenate the sequences.
For example, to generate a 3 bit gray code:
  Write 00, 01, 11, 10
  Prepend 0 => 000, 001, 011, 010
  Prepend 1 => 100, 101, 111, 110
  Write latter in reverse order => 110, 111, 101, 100
  Concatenate => 000, 001, 011, 010, 110, 111, 101, 100

## Slide 23: Truth Table Adjacencies
F = A’
These are adjacent in a gray code sense -
they differ by 1 bit
A’B’ + A’B = A’(B’+B) = A’(1) = A’
A | B | F
0 | 0 | 1
0 | 1 | 1
1 | 0 | 0
1 | 1 | 0
A | B | F
0 | 0 | 0
0 | 1 | 1
1 | 0 | 0
1 | 1 | 1
F = B
Same idea:
A’B + AB = B
Key idea:
Gray code adjacency allows use of simplification theorems
Problem:
Physical adjacency in truth table does not indicate gray code adjacency

## Slide 24: Karnaugh Map Method
0 | 2 | 6 | 4
1 | 3 | 7 | 5
0 | 4 | 12 | 8 | 
1 | 5 | 13 | 9 | 
3 | 7 | 15 | 11 | 
2 | 6 | 14 | 10 | 
A
B
0
1
0
1
0
1
2
3
AB
C
A
A
00
01
11
10
0
1
00
01
11
00
AB CD
00
01
11
10
C
B
D
K-map is an alternative method of representing the truth table that helps visualize adjacencies in up to 6 dimensions
Beyond that, computer-based methods are needed
2-variable K-map
3-variable K-map
4-variable K-map
B
Numbering Scheme: 00, 01, 11, 10
Gray Code — only a single bit changes from code word to next code word
m2 (minterm)

## Slide 25: Visualizing Boolean Cubes
25
Just another way to represent the truth table
n input variables = n dimensional "cube"
3-cube
4-cube
X
011
010
000
001
XYZ 111
110
100
101
Y
Z
0111
0011
0010
0000
0001
0110
1010
0101
0100
1000
1011
1001
1110
WXYZ 1111
1101
1100
Y
Z
W
X
X
1-cube
X
2-cube
01
00
XY 11
10
Y
0
1

## Slide 26: Adjacencies
Adjacent squares differ by exactly one variable
A
BC
0 1
00
AB'C'
01 A'B'C AB'C
11
ABC
10
ABC'
There is wrap-around:
top and bottom rows are adjacent

## Slide 27: 2-Variable Karnaugh Map
A | B | F
0 | 0 | 1
0 | 1 | 1
1 | 0 | 0
1 | 1 | 0

## Slide 28: 2-Variable Karnaugh Map
A | B | F
0 | 0 | 1
0 | 1 | 1
1 | 0 | 0
1 | 1 | 0
A
B
0 1
0
1

## Slide 29: 2-Variable Karnaugh Map
A | B | F
0 | 0 | 1
0 | 1 | 1
1 | 0 | 0
1 | 1 | 0
A
B
0 1
0
1
1
1

## Slide 30: 2-Variable Karnaugh Map
0 | 1
1 | 0
1 | 0
A
B
0
1
A | B | F
0 | 0 | 1
0 | 1 | 1
1 | 0 | 0
1 | 1 | 0

## Slide 31: Rules
•
•
•
•
•
•
•
•
Row and column assignments arranged such that adjacent terms change by only one bit (gray code): use 00,01,11,10 instead of 00,01,10,11
Each map consists of 2n cells, where n is the number of logic variables 2n 1’s can be circled (group) at a time 1, 2, 4, 8, … OK, 3 not OK
No zeros allowed. No diagonals.
Groups should be as large as possible.
Every one must be in at least one group.
Overlapping and "wraps around itself" - i.e. the top and bottom, right and left edges are touching.
Fewest number of groups possible.

## Slide 33: 2-Variable Karnaugh Map
A | B | F
0 | 0 | 1
0 | 1 | 1
1 | 0 | 0
1 | 1 | 0
A
B
0 1
1 | 0
1 | 0
0
1
F = A’B’ + A’B = A’

## Slide 34: Two Level Simplification
F = A’
A asserted, unchanged B varies
G = B'
B complemented, unchanged A varies
F(A,B,C) = A
 |  |  | 0
 | 1 |  | 
 | 1 |  | 0
A
B
0 1
0
1
A
B
0
1
1
1
0
1 0 0
F = A’ B' + A’ B = A’ (B' + B) = A’ G = A' B' + A B' = (A' + A) B' = B'
Key Tool: The Uniting Theorem — A’ (B' + B) = A’
Key Tool: The Uniting Theorem — A’ (B' + B) = A’
Essence of Simplification:
find two element subsets of the ON-set where only one variable changes its value.
This single varying variable can be eliminated!
0 | 0 |  |  |  | 
 |  |  | 1 | 1 | 
0 | 0 |  | 1 | 1 | 
AB C
A
00
01
11
10
0
1
B

## Slide 35: Another Example
A
B
0 1
0 | 1
1 | 1
0
1
F = A’B + AB’ + AB
= (A’B + AB) + (AB’ + AB)
= A + B
A | B | F
0 | 0 | 0
0 | 1 | 1
1 | 0 | 1
1 | 1 | 1

## Slide 36: Another Example
0 | 1
0 | 1
1 | 1
A
B
0
1
A | B | F
0 | 0 | 0
0 | 1 | 1
1 | 0 | 1
1 | 1 | 1
A = 1
B = 1
F = A + B

## Slide 37: Truth Table to Karnaugh Map
A
BC
0 1
00
01
11
10
A | B | C | F
0 | 0 | 0 | 0
0 | 0 | 1 | 0
0 | 1 | 0 | 1
0 | 1 | 1 | 1
1 | 0 | 0 | 0
1 | 0 | 1 | 1
1 | 1 | 0 | 0
1 | 1 | 1 | 1
0 | 0
0 | 1
1 | 1
1 | 0

## Slide 38: 3-Variable Karnaugh Map
1
1
A
BC
1
1
0 | 1
0 | 0
0 | 
 | 0
00
01
11
10
A’BC+A’BC’ = A’B
AB’C+ABC = AC
F = A’B + AC

## Slide 39: Another Example
A’B’C+A’BC = A’C
AB’C’+ABC’ = AC’
F = A’C + AC’ = A  C
A
BC
0 1
00
0 | 1
1 | 0
1 | 0
0 | 1
01
11
10

## Slide 40: Minterm Expansion to K-Map
0 1
00
01
11
10
F = m( 1, 3, 4, 6 )
A A
BC 0 1 BC
00
m0 | m4
m1 | m5
m3 | m7
m2 | m6
01
11
10
0 | 1
1 | 0
1 | 0
0 | 1
Minterms are the 1’s, everything else is 0

## Slide 41: Maxterm Expansion to KMap
0 1
00
01
11
10
BC 0 1 BC
00
M0 | M4
M1 | M5
M3 | M7
M2 | M6
01
11
10
0 | 1
1 | 0
1 | 0
0 | 1
F = ПM( 0, 2, 5, 7 )
A A
Maxterms are the 0’s, everything else is 1

## Slide 42: Yet Another Example
AB’C+ABC = AC
F = B’ + AC
The larger the group of 1’s
the simpler the resulting product term
A
BC
0 1
1 | 1
1 | 1
0 | 1
0 | 0
00
01
A’B’C’+AB’C’+A’B’C+AB’C = B’
11
10

## Slide 43: 4-Variable Karnaugh Map
1
1
1
1
1
1
1
1
1
1
AB
CD
00 01 11 10
00
0
0
0
01
11
10
0
0
0
Note the row
and column orderings.
Required for adjacency
AB
CD
00 01 11 10
00
m0 | m4 | m12 | m8
m1 | m5 | m13 | m9
m3 | m7 | m15 | m11
m2 | m6 | m14 | m10
01
11
10
D
AB’C’
A’BC
F = A’BC + AB’C’ + D

## Slide 44: Find a POS Solution AB
0
0
0
0
0
0
0
CD
00 01 11 10
1 1 | 1 | 1 | 1 1
1 | 1 | 1 | 
00
01
11
10
Find solutions to groups of 0’s to find F’
Invert to get F then use DeMorgan’s
C’D
F’ = C’D + BC’ + AB’CD’
F = (C+D’)(B’+C)(A’+B+C’+D)
AB’CD’
BC’

## Slide 45: Dealing With Don’t Cares
A
BC
0 1
00
01
11
10
F = m(1, 3, 7) + d(0, 5)

## Slide 46: Dealing With Don’t Cares
1
1
x
1
A
BC
0 1
00
x 0
10
0 0
01
A’B’C+AB’C+A’BC+ABC = C
11
F = C
Circle the x’s that help get bigger groups of 1’s (or 0’s if POS) Don’t circle the x’s that don’t
F = m(1, 3, 7) + d(0, 5)