## Slide 1: COMP 122/L Lecture 4 Mahdi Ebrahimi Slides adapted from Dr. Kyle Dewey

## Slide 2: Outline
Two complement
Operations on binary values
  Addition
  Subtraction

## Slide 3: Twos Complement

## Slide 4: Problem
Binary representation so far makes it easy to represent positive numbers and zero
Question:What about representing negative numbers?

## Slide 5: Twos Complement
Way to represent positive integers, negative integers, and zero
If 1 is in the most significant bit (generally leftmost bit in this class), then it is negative

## Slide 6: Decimal to Twos Complement
Example: -5 decimal to binary (twos complement)

## Slide 7: Decimal to Twos Complement
Example: -5 decimal to binary (twos complement)
First, convert the magnitude to an unsigned representation

## Slide 8: Decimal to Twos Complement
Example: -5 decimal to binary (twos complement)
First, convert the magnitude to an unsigned representation
5 (decimal) = 0101 (binary)

## Slide 9: Decimal to Twos Complement
Then, take the bits, and negate them

## Slide 10: Decimal to Twos Complement
Then, take the bits, and negate them
0101

## Slide 11: Decimal to Twos Complement
Then, take the bits, and negate them
~0101 = 1010

## Slide 12: Decimal to Twos Complement
Finally, add one:

## Slide 13: Decimal to Twos Complement
Finally, add one:
1010

## Slide 14: Decimal to Twos Complement
Finally, add one:
1010 + 1 =
1011

## Slide 15: Twos Complement to Decimal
Same operation: negate the bits, and add one

## Slide 16: Twos Complement to Decimal
Same operation: negate the bits, and add one
1011

## Slide 17: Twos Complement to Decimal
Same operation: negate the bits, and add one
~1011 = 0100

## Slide 18: Twos Complement to Decimal
Same operation: negate the bits, and add one
0100

## Slide 19: Twos Complement to Decimal
Same operation: negate the bits, and add one
0100 + 1 =
0101

## Slide 20: Twos Complement to Decimal
Same operation: negate the bits, and add one
0100 + 1 =
0101 =
-5
We started with
1011 - negative

## Slide 21: Intuition
Modular arithmetic, with the convention that a leading 1 bit means negative
000
001
010
011
100
101
110
111
Denotes
+1
Notes: -This is the intuition from Wikipedia, which makes a whole lot more sense

## Slide 22: Intuition
Modular arithmetic, with the convention that a
000
100
101
Denotes
+1
(least -) 111 001 (least +)
110 010
011 (most +) (most -)
leading 1 bit means negative
(zero)
Notes: -This is the intuition from Wikipedia, which makes a whole lot more sense
-There is still a lot of detail missing here - it’s not necessary to understand in order to work with this.
There is actually quite a bit of mathematics behind why this works

## Slide 23: Intuition
Modular arithmetic, with the convention that a
000
Denotes
+1
leading 1 bit means negative
0
001 1
010 2
011 3
100
-4
-3 101
-2 110
-1 111
Notes: -This is the intuition from Wikipedia, which makes a whole lot more sense
-There is still a lot of detail missing here - it’s not necessary to understand in order to work with this.
There is actually quite a bit of mathematics behind why this works

## Slide 24: Negation of 1
000
001
010
011
100
101
110
111
Notes: -Take our wheel from before

## Slide 25: Negation of 1
000
001
010
011
100
101
110
111
Notes: -This is 1

## Slide 26: Negation of 1
000
001
010
011
100
101
110
111
Notes: -Inverted bits

## Slide 27: Negation of 1
000
001
010
011
100
101
110
111
Notes: -Add 1
-This is exactly what we expected - binary 111 represents decimal -1

## Slide 28: Consequences
What is the negation of 000?
000
111 001
110 010
101 011
100
Notes: -Negate all bits: 000 -> 111
-Add one: 000
-Technically, adding one resulted in 1000, but that got cut off

## Slide 29: Consequences
What is the negation of 100?
000
111 001
110 010
101 011
100
Notes: -Negate all bits: 100 -> 011
-Add one: 100
-Uh oh...this states that the negation of -4 is -4.
-Underlying problem is that we don’t have a representation for 4 with just three bits

## Slide 30: Arithmetic Shift Right
Not exactly division by a power of two
Consider -3 / 2
0
000
001 1
010 2
011 3
100
-4
-2 110
-3 101
-1 111
Notes: -101 (-3) shifted right yields 110 (-2), NOT 111 (-1) as expected from typical integer division
-Integer division rounds towards zero, whereas shift right rounds towards negative infinity
-This means they work _identically_ for positive values, but not for negative values (also meaning they are always the same for _unsigned_ values)

## Slide 31: Addition

## Slide 32: Building Up Addition
Question: how might we add the following, in decimal?
986
+123
?

## Slide 33: Building Up Addition
Question: how might we add the following, in decimal?
986
+123
?
6
+3
--
?

## Slide 34
Building Up Addition Question: how might we add the following, in decimal? |  |  | 
 | 986 |  | 
 | +123 |  | 
 | ? |  | 
 |  | 8 | 6
 |  | +2 -- ? | +3 -- 9

## Slide 35
Building Up Addition Question: how might we add the following, in decimal? |  |  | 
 | 986 |  | 
 | +123 |  | 
 | ? |  | 
 | Carry: 1 | 8 | 6
 |  | +2 -- 0 | +3 -- 9

## Slide 36: Building Up Addition
Question: how might we add the following, in decimal?
986
+123
?
6
+3
--
9
8
+2
--
0
1
9
+1
--
?

## Slide 37: Building Up Addition
Question: how might we add the following, in decimal?
986
+123
?
6
+3
--
9
8
+2
--
0
1
9
+1
--
1
Carry: 1

## Slide 38: Building Up Addition
Question: how might we add the following, in decimal?
986
+123
?
6
+3
--
9
8
+2
--
0
1
9
+1
--
1
1
+0
--
1

## Slide 39: Core Concepts
We have a “primitive” notion of adding single digits, along with an idea of carrying digits
We can build on this notion to add numbers together that are more than one digit long

## Slide 40: Now in Binary
Arguably simpler - fewer one-bit possibilities
0 | 0 | 1 | 1
+0 | +1 | +0 | +1
-- | -- | -- | --
? | ? | ? | ?

## Slide 41: Now in Binary
Arguably simpler - fewer one-bit possibilities
0 | 0 | 1 | 1
+0 | +1 | +0 | +1
-- | -- | -- | --
0 | 1 | 1 | 0
Carry: 1

## Slide 42: Chaining the Carry
Also need to account for any input carry
0 | 0 | 0 | 0
0 | 0 | 1 | 1
+0 -- | +1 -- | +0 -- | +1 --
0 | 1 | 1 | 0 Carry: 1
1 | 1 | 1 | 1
0 | 0 | 1 | 1
+0 | +1 | +0 | +1
-- | -- | -- | --
1 | 0 Carry: 1 0 Car |  | ry: 1 1 Carry: 1

## Slide 43: Adding Multiple Bits
How might we add the numbers below?
011
+001

## Slide 44: Adding Multiple Bits
How might we add the numbers below?
0
011
+001
-Need an initial carry-in of zero

## Slide 45: Adding Multiple Bits
How might we add the numbers below?
10
011
+001
0
-Need an initial carry-in of zero

## Slide 46: Adding Multiple Bits
How might we add the numbers below?
110
011
+001
00
-Need an initial carry-in of zero

## Slide 47: Adding Multiple Bits
How might we add the numbers below?
0110
011
+001
100
-Need an initial carry-in of zero

## Slide 48: Adding Multiple Bits
How might we add the numbers below?
0110
011
+001
100
Output Carry Bit
Result Bits
-Need an initial carry-in of zero

## Slide 49: Another Example
111
+001

## Slide 50: Another Example
0
111
+001

## Slide 51: Another Example
10
111
+001
0

## Slide 52: Another Example
110
111
+001
00

## Slide 53: Another Example
1110
111
+001
000
Output Carry Bit
Result Bits
-Now we have an output carry bit of 1. What does this mean?

## Slide 54: Output Carry Bit Significance
For unsigned numbers, it indicates if the result did not fit all the way into the number of bits allotted
May be an error condition for software

## Slide 55: Signed Addition
Question: what is the result of the following operation?
011
+011
?

## Slide 56: Signed Addition
Question: what is the result of the following operation?
011
+011
0110
-If these are treated as signed numbers in two’s complement, then we need a leading 0 to indicate that this is a positive number
-Truncated to three bits, the result is a negative number!

## Slide 57: Overflow
In this situation, overflow occurred: this means that both the operands had the same sign, and the result’s sign differed
011
+011
110
Possibly a software error

## Slide 58: Overflow vs. Carry
These are different ideas
  Carry is relevant to unsigned values
  Overflow is relevant to signed values
Overflow; No Carry
No Overflow; Carry
Overflow; Carry
111 | 011 | 111 | 001
+001 | +011 | +100 | +001
---- | ---- | ---- | ----
000 | 110 | 011 | 010
No Overflow; No Carry
-As to when is it a problem, this all depends on exactly what it is you’re doing

## Slide 59: Subtraction

## Slide 60: Subtraction
Have been saying to invert bits and add one to second operand
Could do it this way in hardware, but there is a trick
001
-001
----
?
001
+111
----
?
Hint: these two questions are equivalent

## Slide 61: Subtraction Trick
Assume we can cheaply invert bits, but we want to avoid adding twice (once to add 1 and once to add the other result)
How can we do this easily?

## Slide 62: Subtraction Trick
Assume we can cheaply invert bits, but we want to avoid adding twice (once to add 1 and once to add the other result)
How can we do this easily?
  Set the initial carry to 1 instead of 0

## Slide 63: Subtraction Example
0101
-0011

## Slide 64: Subtraction Example
0101
-0011
Invert 0011

## Slide 65: Subtraction Example
0101
-0011
Invert 0011
1100

## Slide 66: Subtraction Example
0101
-0011
Invert 0011
1100
Equivalent to

## Slide 67: Subtraction Example
0101
-0011
Invert 0011
1100
Equivalent to
1
0101
+1100
-An initial carry-in of 1 is equivalent to adding 1 and then adding the other operand

## Slide 68: Subtraction Example
0101
-0011
Invert 0011
1100
Equivalent to
+1100
0010
11011
0101
-An initial carry-in of 1 is equivalent to adding 1 and then adding the other operand