## Slide 1: Number Systems and Number Representation (Rational Numbers)
1

## Slide 2: Agenda
Number Systems
Finite representation of unsigned integers Finite representation of signed integers
Finite representation of rational numbers

## Slide 3: Number Systems
So far, we have studied the following integer number systems in computer
  Unsigned numbers
  Sign/magnitude numbers
  Two’s complement numbers
What about rational numbers?
A rational number is one that can be expressed as the ratio of two integers
Infinite range and precision
For example, 2.5, -10.04, 0.75 etc

## Slide 4: Rational Numbers
Computer science
Finite range and precision
Approximate using floating point number
  Binary point “floats” across bits
Two common notations to represent rational numbers in computer
  Fixed-point numbers
  Floating-point numbers

## Slide 5: Fixed-Point Numbers
Fixed point notation has an implied binary point between the integer and fraction bits
  The binary point is not a part of the representation but is implied
  Example:
    Fixed-point representation of 6.75 using 4 integer bits and 4 fraction bits:
The number of integer and fraction bits must be agreed upon by those generating and those reading the number
  There is no way of knowing the existence of the binary point except through agreement of those people interpreting the number

## Slide 6: Signed Fixed-Point Numbers
As with whole numbers, negative fractional numbers can be represented in two ways
  Sign/magnitude notation
  Two’s complement notation
Example:
  -2.375 using 8 bits (4 bits each to represent integer and fractional parts)
    2.375 = 0010 . 0110
    Sign/magnitude notation: 1010 0110
    Two’s complement notation:
  1. flip all the bits: 1101 1001
  2. add 1: + 1
  1101 1010
Addition and subtraction works easily in computer with 2’s complement notation like integer addition and subtraction

## Slide 7: Example
Suppose that we have 8 bits to represent a number
  4 bits for integer and 4 bits for fraction
Compute 0.75 + (-0.625)
  0.75 = 0000 1100
  0.625 = 0000 1010
  -0.625 in 2’s complement form: 1111 0110
  0.75 0000 1100
  + - 0.625 1111 0110
  0000 0010
0.125

## Slide 8: Fixed-Point Number Systems
Fixed-point number systems have a limitation of having a constant number of integer and fractional bits
Some low-end digital signal processors support fixed-point numbers
  Example: TMS320C550x TI (Texas Instruments) DSPs: www.ti.com

## Slide 9: Floating-Point Numbers
Floating-point number systems circumvent the limitation of having a constant number of integer and fractional bits
  They allow the representation of very large and very small numbers
The binary point floats to the right of the most significant 1
  Similar to decimal scientific notation
  For example, write 27310 in scientific notation:
    Move the decimal point to the right of the most significant digit and increase the exponent:
  273 = 2.73 × 102
In general, a number is written in scientific notation as:
± M × BE
Where,
  M = mantissa
  B = base
  E = exponent
  In the example, M = 2.73, B = 10, and E = 2 (that is, +2.73 × 102)

## Slide 10: Floating-Point Numbers
Floating-point number representation using 32 bits
  1 sign bit
  8 exponent bits
  23 bits for the mantissa.
The following slides show three versions of floating-point representation with 22810 using a 32-bit
  The final version is called the IEEE 754 floating-point standard

## Slide 11: Floating-Point Representation #1
First, convert the decimal number to binary
  22810 = 111001002 = 1.11001 × 27
Next, fill in each field in the 32-bit:
  The sign bit (1 bit) is positive, so 0
  The exponent (8 bits) is 7 (111)
  The mantissa (23 bits) is 1.11001
/ Fraction

## Slide 12: Floating-Point Representation #2
You may have noticed that the first bit of the mantissa is always 1, since the binary point floats to the right of the most significant 1
  Example: 22810 = 111001002 = 1.11001 × 27
Thus, storing the most significant 1 (also called the implicit leading 1) is redundant information
We can store just the fraction parts in the 23-bit field
  Now, the leading 1 is implied
0 0 0 0 0 1 1 1
Mantissa /

## Slide 13: Floating-Point Representation #3
  The exponent needs to represent both positive and negative
The final change is to use a biased exponent
  The IEEE 754 standard uses a bias of 127
  Biased exponent = bias + exponent
    For example, an exponent of 7 is stored as 127 + 7 = 134 = 100001102
Thus, 22810 using the IEEE 754 32-bit floating-point standard is
Most general purpose processors (including Intel and AMD processors) provide hardware support for double-precision floating-point numbers and operations
Mantissa /
22810 = 111001002 = 1.11001 × 27

## Slide 14: IEEE Floating Point Representation
Common finite representation: IEEE floating point
More precisely: ISO/IEEE 754 standard
Using 32 bits (type float in C):
1 bit: sign (0=>positive, 1=>negative)
8 bits: exponent + 127
23 bits: binary fraction of the form 1.ddddddddddddddddddddddd
Using 64 bits (type double in C):
1 bit: sign (0=>positive, 1=>negative)
11 bits: exponent + 1023
52 bits: binary fraction of the form 1.dddddddddddddddddddddddddddddddddddddddddddddddddddd
Mantissa /

## Slide 15: Example
Represent -5810 using the IEEE 754 floating-point standard
  First, convert the decimal number to binary
    5810 = 1110102 = 1.1101 × 25
  Next, fill in each field in the 32-bit number
    The sign bit is negative (1)
    The 8 exponent bits are (127 + 5) = 132 = 10000100(2)
    The remaining 23 bits are the fraction bits: 11010000...000(2)
  It is 0xC2680000 in the hexadecimal form
    Check this out with the result of the sample program in the slide# 3

## Slide 16: Double Precision Example
Represent -5810 using the IEEE 754 double precision
  First, convert the decimal number to binary
    5810 = 1110102 = 1.1101 × 25
  Next, fill in each field in the 64-bit number
    The sign bit is negative (1)
    The 11 exponent bits are (1023 + 5) = 1028 = 10000000100(2)
    The remaining 52 bits are the fraction bits: 11010000...000(2)
  It is 0xC04D000000000000 in the hexadecimal form

## Slide 17: Floating-Point Numbers: Special Cases
The IEEE 754 standard includes special cases for numbers that are difficult to represent, such as 0 because it lacks an implicit leading 1
Number | Sign | Exponent | Fraction
0 | X | 00000000 | 00000000000000000000000
∞ | 0 | 11111111 | 00000000000000000000000
- ∞ | 1 | 11111111 | 00000000000000000000000
NaN | X | 11111111 | non-zero
  NaN is used for numbers that don’t exist, such as √-1 or log(-5)

## Slide 18: Floating Point Example
Sign (1 bit):
1 => negative
Exponent (8 bits):
10000011B = 131
131 – 127 = 4
Fraction (23 bits):
1.10110110000000000000000B
1 +
(1*2-1)+(0*2-2)+(1*2-3)+(1*2-4)+(0*2-5)+(1*2-6)+(1*2-7)
= 1.7109375
Number:
-1.7109375 * 24 = -27.375
11000001110110110000000000000000
32-bit representation
Notes: https://www.youtube.com/watch?v=LXF-wcoeT0o

## Slide 19: Floating Point Example
263
2
131
2
65
2
32
2
16
2
8
2
4
2
2
2
1
2
0
1
1
1
0
0
0
0
0
1
263: 100000111
0.3 * 2 | 0.6 | 0
0.6 * 2 | 1.2 | 1
0.2 * 2 | 0.4 | 0
0.4 * 2 | 0.8 | 0
0.8 * 2 | 1.6 | 1
0.6 * 2 | 1.2 | 1
 |  | 0
 |  | 0
 |  | 1
 |  | 1
 |  | 0
0.3 : 01001100110011….
263.3
Stop when it gets 1.0
IEEE754 floating-point standard can’t represent some numbers exactly

## Slide 20: Floating Point Example
0100 0011 1000 0011 1010 0110 0110 0110
32-bit representation
263.3
100000111.0100110011…
2) Scientific notation:
1.000001110100110011… * 28
Mantissa
Sign (1 bit):
positive => 0
Exponent (8 bits):
127 + 8 = 135
135 = 10000111B
Fraction (23 bits):
00000111010011001100110
Notes: https://www.youtube.com/watch?v=8afbTaA-gOQ

## Slide 21: Binary Coded Decimal (BCD)
Since floating-point number systems can’t represent some numbers exactly such as 0.3, some application (calculators) use BCD (Binary coded decimal)
  BCD numbers encode each decimal digit using 4 bits with a range of 0 to 9
  BCD fixed-point notation examples
    1.7 = 0001 . 0111
    4.9 = 0100 . 1001
BCD is very common in electronic systems where a numeric value is to be displayed, especially, in systems consisting solely of digital logic (not containing a microprocessor) - Wiki
Decimal | BCD Digit
0 | 0000
1 | 0001
2 | 0010
3 | 0011
4 | 0100
5 | 0101
6 | 0110
7 | 0111
8 | 1000
9 | 1001
6.75 = 0110.01110101

## Slide 22: Converting Between Decimal and Binary Floating-Point Numbers
https://kyledewey.github.io/comp122-fall17/lecture/week_2/floating_point_interconversions.html