## Slide 1: COMP 122/L Lecture 6 Mahdi Ebrahimi Slides adapted from Dr. Kyle Dewey

## Slide 2: Assembly

## Slide 3: Core Components
Some place to hold the statements as we operate on them
Some place to hold which statement is next
Some place to hold variables
Some way to add numbers

## Slide 4: Processors
Amazingly, these are all the core components of a processor
  Why is this significant?
Processors just reads a series of statements (instructions) forever.

## Slide 5: Core Components
Some place to hold the statements as we operate on them
Some place to hold which statement is next
Some place to hold variables
Some way to add numbers

## Slide 6: Core Components
Some place to hold the statements as we operate on them - memory
Some place to hold which statement is next -
program counter
Some place to hold variables - registers
  Behave just like variables with fixed names
Some way to add numbers – arithmetic logic unit (ALU)
Some place to hold which statement is currently being executed – instruction register (IR)

## Slide 7: Basic Interaction
Copy instruction from memory at wherever the program counter says into the instruction register
Execute it, possibly involving registers and the arithmetic logic unit
Update the program counter to point to the next instruction
Repeat

## Slide 8: Basic Interaction
initialize(); while (true) {
instruction_register = memory[program_counter];
execute(instruction_register); program_counter++;
}
-initialize() will load in the initial state, and put instructions in memory
-execute(instruction_register) will read the instruction and do what it says, potentially looking at registers, assigning things to registers, and using the arithmetic logic unit
-Have this handy while going through next animation

## Slide 9
ARM
https://en.wikipedia.org/wiki/ARM_architecture
Notes: ARM: Advanced RISC Machine, originally Acorn RISC Machine
Reduced Instruction Set Computer, or RISC (/rɪsk/),

## Slide 10: Why ARM?
Incredibly popular in embedded devices
Much simpler than Intel processors
-Embedded devices include things like phones and microwaves.
-Your computer may have an ARM processor in it even though the “main” processor is from Intel
Notes: ARM: Advanced RISC Machine, originally Acorn RISC Machine
Reduced Instruction Set Computer, or RISC (/rɪsk/),

## Slide 11: Code on ARM
x = 5;
y = 7;
z = x + y;
Original
ARM
mov | r0, | #5 | 
mov | r1, | #7 | 
add | r2, | r0, | r1

## Slide 12: Code on ARM
Original
ARM
mov | r0, | #5 | 
mov | r1, | #7 | 
add | r2, | r0, | r1
x = 5;
y = 7;
z = x + y;
move: put the given value into a register
r0: register 0

## Slide 13: Code on ARM
Original
ARM
mov | r0, | #5 | 
mov | r1, | #7 | 
add | r2, | r0, | r1
x = 5;
y = 7;
z = x + y;
move: put the given value into a register
r1: register 1

## Slide 14: Code on ARM
Original
ARM
mov | r0, | #5 | 
mov | r1, | #7 | 
add | r2, | r0, | r1
x = 5;
y = 7;
z = x + y;
add: add the rightmost registers, putting the result in the first register
r2: register 2

## Slide 15: Available Registers
17 registers in all
  16 “general-purpose”
  1 “special-purpose”
For the moment, we will only consider registers r0 - r12
-General purpose: can put values in them and take values out as I please
-Special purpose: holding certain flags. Can manipulate this, but not in the same way as a general-purpose register

## Slide 16: Assembly
The code that you see below is ARM assembly
Assembly is *almost* what the machine sees. For the most part, it is a direct translation to binary from here (known as machine code)
mov | r0, | #5 | 
mov | r1, | #7 | 
add | r2, | r0, | r1
-More on why I said “the most part” later. Psuedo instructions are translated to other instructions. Branches also need calculation to occur (for labels), and there are caveats about the instruction immediately after a branch

## Slide 17: Workflow
Assembler (analogous to a compiler)
Machine Code
001101....
Assembly |  |  | 
mov mov add | r0, r1, r2, | #5 #7 r0, | r1

## Slide 18: Machine Code
This is what the process actually executes and accepts as input
Each instruction is represented with 32 bits
add r2, r0, r1
-Converting to machine code is mostly one-to-one: just put the right bits in the right places
-There are some exceptions where we have to be a bit smarter, but not much smarter. Assemblers are nowhere near as complex as compilers.

## Slide 19: Adding More Functionality
We need a way to display the result
What does this entail?
-Actually quite the tall order

## Slide 20: Adding More Functionality
We need a way to display the result
What does this entail?
  Input / output. This entails talking to devices, which the operating system handles
  We need a way to tell the operating system to kick in
-Actually quite the tall order

## Slide 21: Talking to the OS
We are going to be running on an ARM simulator, ARMSim#
We cannot directly access system libraries (they aren’t even in the same machine language)
How might we print something?

## Slide 22: ARMSim# Routines
ARM features a swi instruction, which triggers a software interrupt
Outside of a simulator, these pause the program and tell the OS to check something
Inside the simulator, it tells the simulator to check something
Notes: SWI stands for Software Interrupt. In RISC OS SWIs are used to access Operating System routines or modules produced by a 3rd party.

## Slide 23: swi
So we have the OS/simulator’s attention. But how does it know what we want?

## Slide 24: swi
So we have the OS/simulator’s attention. But how does it know what we want?
  swi operand: integer saying what to do
  The OS/simulator can also read the registers to get extra information as needed
-”Integer saying what to do”: e.g., we agree that “5” means “print something”
-With reading the registers, these could include exactly what to print

## Slide 25: (Finally) Printing an Integer
For ARMSim#, the integer that says “print an integer” is 0x6B
Register r1 holds the integer to print
Register r0 holds where to print it; 1
means “print to standard output (screen)”
-Other SPIM utilities available via syscall: https://www.doc.ic.ac.uk/lab/secondyear/spim/ node8.html

## Slide 26: Augmenting with Printing
mov mov add | r0, r1, r2, | #5 #7 r0, | r1 | 
mov | r1, | r2 | ; | r1: integer to print
mov swi | r0, 0x6B | #1 | ; ; | r0: where to print it 0x6B: print integer

## Slide 27: Exiting
If you are using ARMSim#, then you need to say when you are done as well
How might this be done?

## Slide 28: Exiting
If you are using ARMSim#, then you need to say when you are done as well
How might this be done?
  swi with a particular operand (specifically 0x11)

## Slide 29: Augmenting with Exiting
mov mov add | r0, r1, r2, | #5 #7 r0, | r1 |  |  | 
mov | r1, | r2 | ; | r1: integer to print |  | 
mov swi | r0, 0x6B | #1 | ; ; | r0: where to print it 0x6B: print integer |  | 
swi | 0x11 | ; |  | 0x11: | exit | program

## Slide 30: Making it a Full Program
Everything is just a bunch of bits
We need to tell the assembler which bits should be placed where in memory

## Slide 31
-Image source: https://en.wikipedia.org/wiki/Data_segment
-Representation of a program in memory
-What do you recognize?

## Slide 32: Allocated as Program Runs
-Image source: https://en.wikipedia.org/wiki/Data_segment
-You’ve seen these two before
-What might the rest be?

## Slide 33: Everything Below is Allocated at Program Load
Constants (e.g., strings)
Mutable Global Variables
Code
Allocated as Program Runs
-Image source: https://en.wikipedia.org/wiki/Data_segment

## Slide 34: Process Memory Map

## Slide 35: Marking Code
mov mov add mov | r0, r1, r2, r1, | #5 #7 r0, r1 r2
mov swi | r0, 0x6B | #1
swi | 0x11 | 
Use a .text directive to specify code section
.text
-Directives tell the assembler to do something

## Slide 36: Marking Code
Use a .data directive to specify data section
.data string1:
.asciz “hello” string2:
.asciz “bye”
-Directives tell the assembler to do something