## Slide 1: COMP 122/L Lecture 9 Mahdi Ebrahimi Slides adapted from Dr. Kyle Dewey

## Slide 2: Outline
The compare (cmp) instruction
Conditionally-executed instructions
Translating simple if statements

## Slide 3: The compare (cmp) instruction

## Slide 4: Compare (cmp)
Subtracts two given operands, discarding the result.
However, the status bits (e.g., carry, zero, etc.) get set.
Syntax
CMP Rn, Operand2
where:
Rn is the ARM register holding the first operand.
Operand2 is a flexible second operand.
Operation
These instructions compare the value in a register with Operand2. They update the condition flags on the result, but do not place the result in any register.
The CMP instruction subtracts the value of Operand2 from the value in Rn. This is the same as a SUBS instruction, except that the result is discarded.
Notes: Syntax
CMP{cond} Rn, Operand2
where:
cond is an optional condition code.
Rn is the ARM register holding the first operand.
Operand2 is a flexible second operand.
Operation
These instructions compare the value in a register with Operand2. They update the condition flags on the result, but do not place the result in any register.
The CMP instruction subtracts the value of Operand2 from the value in Rn. This is the same as a SUBS instruction, except that the result is discarded.

## Slide 5: Compare (cmp)
Subtracts two given operands, discarding the result.
However, the status bits (e.g., carry, zero, etc.) get set.
mov | r0, | #5
cmp | r0, | #5

## Slide 6: Compare (cmp)
Subtracts two given operands, discarding the result.
However, the status bits (e.g., carry, zero, etc.) get set.
mov r0, #5
cmp r0, #5
Sets zero bit/flag (result is zero)

## Slide 7: Compare (cmp)
Subtracts two given operands, discarding the result.
However, the status bits (e.g., carry, zero, etc.) get set.
mov | r0, | #5
cmp | r0, | #5
mov | r0, | #5
cmp | r0, | #20
Sets zero bit/flag (result is zero)

## Slide 8: Compare (cmp)
Subtracts two given operands, discarding the result.
However, the status bits (e.g., carry, zero, etc.) get set.
mov r0, #5
cmp r0, #5
Sets zero bit/flag (result is zero)
mov r0, #5
cmp r0, #20
Sets negative bit/flag (result is negative)

## Slide 9: Significance Status bits say something about the result of arithmetic comparisons

## Slide 10: Significance
Status bits say something about the result of arithmetic comparisons
mov r0, #5
cmp r0, #5
Sets zero bit/flag (result is zero)

## Slide 11: Significance
Status bits say something about the result of arithmetic comparisons
mov r0, #5
cmp r0, #5
Sets zero bit/flag (result is zero)
Operands must have been equal.

## Slide 12: Significance
Status bits say something about the result of arithmetic comparisons
mov r0, #5
cmp r0, #5
Sets zero bit/flag (result is zero)
Operands must have been equal.
mov r0, #5
cmp r0, #20
Sets negative bit/flag (result is negative)

## Slide 13: Significance
Status bits say something about the result of arithmetic comparisons
mov r0, #5
cmp r0, #5
Sets zero bit/flag (result is zero)
Operands must have been equal.
mov r0, #5
cmp r0, #20
Sets negative bit/flag (result is negative)
First operand must be < second.

## Slide 14: Conditionally-executed instructions

## Slide 15: Conditionally-Executed Instructions ARM allows for instructions to be conditionally executed, depending on the values of the status bits.

## Slide 16: Conditionally-Executed Instructions
ARM allows for instructions to be conditionally executed, depending on the values of the status bits.
movmi r0, #42

## Slide 17: Conditionally-Executed Instructions
ARM allows for instructions to be conditionally executed, depending on the values of the status bits.
movmi r0, #42
move if the negative bit is set

## Slide 18: Conditionally-Executed Instructions
ARM allows for instructions to be conditionally executed, depending on the values of the status bits.
movmi r0, #42
move if the negative bit is set
movpl r1, #23

## Slide 19: Conditionally-Executed Instructions
ARM allows for instructions to be conditionally executed, depending on the values of the status bits.
movmi r0, #42
move if the negative bit is set
movpl r1, #23
move if the negative bit is not set

## Slide 20: Conditionally-Executed Instructions
ARM allows for instructions to be conditionally executed, depending on the values of the status bits.
moveq r0, #42

## Slide 21: Conditionally-Executed Instructions
ARM allows for instructions to be conditionally executed, depending on the values of the status bits.
moveq r0, #42
move if the zero bit is set

## Slide 22: Conditionally-Executed Instructions
ARM allows for instructions to be conditionally executed, depending on the values of the status bits.
moveq r0, #42
move if the zero bit is set
movne r0, #42

## Slide 23: Conditionally-Executed Instructions
ARM allows for instructions to be conditionally executed, depending on the values of the status bits.
moveq r0, #42
move if the zero bit is set
movne r0, #42
move if the zero bit is not set

## Slide 25: Example: conditional_execution.s

## Slide 26: Translating simple if statements

## Slide 28: Example 1

## Slide 29: Example 2

## Slide 30: Translating if
Simple ifs can be translated with conditionally-executed instructions
Example:
  AbsoluteValue.java
  absolute_value.s