## Slide 1: COMP 122/L Lecture 12 Mahdi Ebrahimi Slides adapted from Dr. Kyle Dewey

## Slide 2: Outline
Memory instructions
  Load (ldr)
  Store (str)
Arrays

## Slide 3: Memory Operations

## Slide 4: Refresher You’ve already seen one form of ldr for handling strings

## Slide 5: Refresher
You’ve already seen one form of ldr for handling strings
.data my_string:
.asciz “hello”
.text
ldr r0, =my_string

## Slide 6: Refresher
You’ve already seen one form of ldr for handling strings
.data my_string:
.asciz “hello”
.text
ldr r0, =my_string
Puts starting address of “hello” in r0
-This was used for setting up swi instructions
-While this uses memory, it did so indirectly (the swi instruction actually read the memory, not us)

## Slide 7: Putting Integers in Memory
.word directive will put a 32-bit integer in memory, much like .asciz will put a string in memory

## Slide 8: Putting Integers in Memory
.word directive will put a 32-bit integer in memory, much like .asciz will put a string in memory
.data my_string:
.asciz “hello” first_int:
.word 42 second_int:
.word 38

## Slide 9: Step 1: use ldr to put its address into a register...
Reading Integers From Memory

## Slide 10: Reading Integers From Memory
Step 1: use ldr to put its address into a register...
.data first_int:
.word 42 second_int:
.word 38
.text
ldr r0, =first_int

## Slide 11
Step 2: use ldr with [] to read the value at the address
.data first_int:
.word 42 second_int:
.word 38
.text
ldr r0, =first_int
Reading Integers From Memory

## Slide 12
Step 2: use ldr with [] to read the value at the address
.data first_int:
.word 42 second_int:
.word 38
.text
ldr r0, =first_int ldr r1, [r0]
Reading Integers From Memory

## Slide 13
Step 2: use ldr with [] to read the value at the address
.data first_int:
.word 42 second_int:
.word 38
.text
ldr r0, =first_int ldr r1, [r0]
r1: 42
Reading Integers From Memory

## Slide 14: Writing Integers to Memory Step 1: use ldr to put its address into a register...

## Slide 15: Writing Integers to Memory
Step 1: use ldr to put its address into a register...
.data first_int:
.word 42 second_int:
.word 38
.text
ldr r0, =first_int

## Slide 16: Writing Integers to Memory
Step 2: use str to write a value at that address
.data first_int:
.word 42 second_int:
.word 38
.text
ldr r0, =first_int

## Slide 17: Writing Integers to Memory
Step 2: use str to write a value at that address
.data first_int:
.word 42 57
second_int:
.word 38
.text
ldr r0, =first_int mov r1, #57
str r1, [r0]

## Slide 18: Example: memory_variables.s

## Slide 19: Arrays

## Slide 20: Specifying Arrays
Only distinction from variables:
multiple values are specified with the .word directive

## Slide 21: Specifying Arrays
Only distinction from variables:
multiple values are specified with the .word directive
.data first_int:
.word 42

## Slide 22: Specifying Arrays
Only distinction from variables:
multiple values are specified with the .word directive
.data first_int:
.word 42 array:
.word 32, 65, 76, 87

## Slide 23: Accessing Arrays Basic approach: increment memory address

## Slide 24: Accessing Arrays
Basic approach: increment memory address
.data arr:
.word .text ldr r0, | 32, =arr | 65, 76
ldr r1, | [r0] | 
add r0, | r0, | #4
ldr r2, | [r0] | 
add r0, | r0, | #4
ldr r3, | [r0] | 
-Offsets increment by 4 because one word is 4 bytes

## Slide 25: Accessing Arrays
r1: 32
r2: 65
r3: 76
Basic approach: increment memory address
.data arr:
.word 32, 65, 76
.text
ldr r0, =arr ldr r1, [r0]
add | r0, | r0, | #4
ldr | r2, | [r0] | 
add | r0, | r0, | #4
ldr | r3, | [r0] | 

## Slide 26: Accessing Arrays
Basic approach: increment memory address
.data arr:
.word 32, 65, 76
.text
ldr r0, =arr ldr r1, [r0]
add | r0, | r0, | #4
ldr | r2, | [r0] | 
add | r0, | r0, | #4
ldr | r3, | [r0] | 
r1: 32
r2: 65
r3: 76
32 | 65 | 76
arr | arr + 4 | arr + 8
-Top right corner shows memory layout in terms of arr

## Slide 27: Example: register_indirect.s

## Slide 28: More on Memory Access
ldr r3, [r0]
The above instruction uses the register indirect addressing mode
  Addressing mode: how the processor accesses something
  Register indirect: Memory access is done through an address in a register
Many more available: see register_*.s
-See also https://www.cs.uregina.ca/Links/class-info/301/ARM-addressing/lecture.html

## Slide 29: ARM addressing Modes
https://www.cs.uregina.ca/Links/class-info/301/ARM-addressing/lecture.html

## Slide 30: ARM addressing Modes
https://www.cs.uregina.ca/Links/class-info/301/ARM-addressing/lecture.html
Addressing Mode Assembly Mnemonic Effective address FinalValue in R1
---------------------------------------------------------------------------------------------------------------------------------
Indexed, base LDR R0, [R1] R1 R1
Register indirect
---------------------------------------------------------------------------------------------------------------------------------
Pre-indexed, LDR R0, [R1, #d] R1 + d R1
base with displacement
----------------------------------------------------------------------------------------------------------------------------------
Pre-indexed, LDR R0, [R1, #d]! R1 + d R1 + d
autoindexing
----------------------------------------------------------------------------------------------------------------------------------
Post-indexed, LDR R0, [R1], #d R1 R1 + d
autoindexed
----------------------------------------------------------------------------------------------------------------------------------
Double Reg indirect LDR R0, [R1, R2] R1 + R2 R1
----------------------------------------------------------------------------------------------------------------------------------
Double Reg indirect LDR R0, [R1, R2, LSL #2] R1 + (R2 * 4) R1 (R2 also unchanged)
with scaling
----------------------------------------------------------------------------------------------------------------------------------

## Slide 31: Array Access Example: print_array_fixed_length.s

## Slide 32: Writing to Array Example: write_array_increasing.s

## Slide 33: Another Array Access Example: print_array_variable_length.s