## Slide 1: COMP 122/L Lecture 17 Mahdi Ebrahimi Slides adapted from Dr. Kyle Dewey

## Slide 2: Outline
Boolean formulas and truth tables
Introduction to circuits

## Slide 3: Boolean Formulas and Truth Tables

## Slide 4: Boolean?
Binary: true and false
  Abbreviation: 1 and 0
  Easy for a circuit: on or off
Serves as the building block for all digital circuits

## Slide 5
Basic Operation: AND
AB == A AND B

## Slide 6: Basic Operation: AND
AB == A AND B
true only if both A and B are true

## Slide 7: Basic Operation: AND
A | B | AB
0 | 0 | 0
0 | 1 | 0
1 | 0 | 0
1 | 1 | 1
AB == A AND B
true only if both A and B are true
Truth Table:

## Slide 8
Basic Operation: OR
A + B == A OR B

## Slide 9: Basic Operation: OR
A + B == A OR B
false only if both A and B are false

## Slide 10: Basic Operation: OR
A | B | A + B
0 | 0 | 0
0 | 1 | 1
1 | 0 | 1
1 | 1 | 1
A + B == A OR B
false only if both A and B are false
Truth Table:

## Slide 11
Basic Operation: NOT
!A == A’ == A == NOT A

## Slide 12: Basic Operation: NOT
!A == A’ == A == NOT A
Flip the result of the operand

## Slide 13: Basic Operation: NOT
!A == A’ == A == NOT A
Flip the result of the operand
Truth Table:
A | !A
0 | 1
1 | 0

## Slide 14: AND, OR, and NOT
Serve as the basis for everything we will do in this class
As simple as they are, they can do just about everything we want

## Slide 15: Truth Table to Formula
Idea: for every output in the truth table which has a 1, write an AND which corresponds to it
String them together with OR

## Slide 16: Truth Table to Formula
Idea: for every output in the truth table which has a 1, write an AND which corresponds to it
String them together with OR
A | B | Out
0 | 0 | 1
0 | 1 | 0
1 | 0 | 0
1 | 1 | 1
-For example, consider this table

## Slide 17: Truth Table to Formula
Idea: for every output in the truth table which has a 1, write an AND which corresponds to it
String them together with OR
A | B | Out
0 | 0 | 1
0 | 1 | 0
1 | 0 | 0
1 | 1 | 1
-First 1 in the table

## Slide 18: Truth Table to Formula
Idea: for every output in the truth table which has a 1, write an AND which corresponds to it
String them together with OR
!A!B
A | B | Out
0 | 0 | 1
0 | 1 | 0
1 | 0 | 0
1 | 1 | 1
-This corresponds to !A!B
-That is, the output is set to 1 when !A!B is true (meaning when A = 0 and B = 0)

## Slide 19: Truth Table to Formula
Idea: for every output in the truth table which has a 1, write an AND which corresponds to it
String them together with OR
!A!B
A | B | Out
0 | 0 | 1
0 | 1 | 0
1 | 0 | 0
1 | 1 | 1
-Second 1 in the table

## Slide 20: Truth Table to Formula
Idea: for every output in the truth table which has a 1, write an AND which corresponds to it
String them together with OR
!A!B
AB
A | B | Out
0 | 0 | 1
0 | 1 | 0
1 | 0 | 0
1 | 1 | 1
-This corresponds to AB

## Slide 21: Truth Table to Formula
Idea: for every output in the truth table which has a 1, write an AND which corresponds to it
String them together with OR
!A!B + AB
A | B | Out
0 | 0 | 1
0 | 1 | 0
1 | 0 | 0
1 | 1 | 1
-Finally, string them together with OR

## Slide 22: Truth Table to Formula
A | B | Out
0 | 0 | 1
0 | 1 | 0
1 | 0 | 0
1 | 1 | 1
Idea: for every output in the truth table which has a 1, write an AND which corresponds to it
String them together with OR
Out = !A!B + AB
-Out is equal to this formula

## Slide 23: Sum of Products Notation
This formula is in sum of products notation:
Out = !A!B + AB

## Slide 24: Sum of Products Notation
This formula is in sum of products notation:
Out = !A!B + AB
Sum

## Slide 25: Sum of Products Notation
This formula is in sum of products notation:
Out = !A!B + AB
Sum
Products

## Slide 26: Sum of Products Notation
This formula is in sum of products notation:
Out = !A!B + AB
Sum
Products
Very closely related to the sort of sums and products you’re more familiar with...more on that later.

## Slide 27
Bigger Operations
Adding single bits with a carry-in and a carry-out (Cout)

## Slide 28: Bigger Operations
Adding single bits with a carry-in and a carry-out (Cout)
0
1
1
0 | 0 | 0 | 0
0 | 0 | 1 | 1
+0 | +1 | +0 | +1
-- Cout: 0 | -- Cout: 0 | -- Cout: 0 | -- Cout: 1 0
1 | 1 | 1 | 1
0 | 0 | 1 | 1
+0 -- 1 Cout: 0 | +1 -- 0 Cout: 1 | +0 -- 0 Cout: 1 | +1 -- 1 Cout: 1

## Slide 29
Single Bit Addition as a Truth Table
Inputs?

## Slide 30: Single Bit Addition as a Truth Table
Inputs?
Carry-in, first operand bit, second operand bit.

## Slide 31: Single Bit Addition as a Truth Table
Inputs?
Carry-in, first operand bit, second operand bit.
Outputs?

## Slide 32: Single Bit Addition as a Truth Table
Inputs?
Carry-in, first operand bit, second operand bit.
Outputs?
Result bit, carry-out bit.

## Slide 33: Single Bit Addition as a Truth Table
A | B | Cin | R | Cout
0 | 0 | 0 |  | 
0 | 0 | 1 |  | 
0 | 1 | 0 |  | 
0 | 1 | 1 |  | 
1 | 0 | 0 |  | 
1 | 0 | 1 |  | 
1 | 1 | 0 |  | 
1 | 1 | 1 |  | 

## Slide 34: Single Bit Addition as a Truth Table
A | B | Cin | R | Cout
0 | 0 | 0 |  | 
0 | 0 | 1 |  | 
0 | 1 | 0 |  | 
0 | 1 | 1 |  | 
1 | 0 | 0 |  | 
1 | 0 | 1 |  | 
1 | 1 | 0 |  | 
1 | 1 | 1 |  | 
0
0
+0
--

## Slide 35: Single Bit Addition as a Truth Table
A | B | Cin | R | Cout
0 | 0 | 0 | 0 | 0
0 | 0 | 1 |  | 
0 | 1 | 0 |  | 
0 | 1 | 1 |  | 
1 | 0 | 0 |  | 
1 | 0 | 1 |  | 
1 | 1 | 0 |  | 
1 | 1 | 1 |  | 
0
0
+0
--
0 Cout: 0

## Slide 36: Single Bit Addition as a Truth Table
A | B | Cin | R | Cout
0 | 0 | 0 | 0 | 0
0 | 0 | 1 | 1 | 0
0 | 1 | 0 |  | 
0 | 1 | 1 |  | 
1 | 0 | 0 |  | 
1 | 0 | 1 |  | 
1 | 1 | 0 |  | 
1 | 1 | 1 |  | 

## Slide 37: Single Bit Addition as a Truth Table
A | B | Cin | R | Cout
0 | 0 | 0 | 0 | 0
0 | 0 | 1 | 1 | 0
0 | 1 | 0 | 1 | 0
0 | 1 | 1 |  | 
1 | 0 | 0 |  | 
1 | 0 | 1 |  | 
1 | 1 | 0 |  | 
1 | 1 | 1 |  | 

## Slide 38: Single Bit Addition as a Truth Table
A | B | Cin | R | Cout
0 | 0 | 0 | 0 | 0
0 | 0 | 1 | 1 | 0
0 | 1 | 0 | 1 | 0
0 | 1 | 1 | 0 | 1
1 | 0 | 0 |  | 
1 | 0 | 1 |  | 
1 | 1 | 0 |  | 
1 | 1 | 1 |  | 

## Slide 39: Single Bit Addition as a Truth Table
A | B | Cin | R | Cout
0 | 0 | 0 | 0 | 0
0 | 0 | 1 | 1 | 0
0 | 1 | 0 | 1 | 0
0 | 1 | 1 | 0 | 1
1 | 0 | 0 | 1 | 0
1 | 0 | 1 |  | 
1 | 1 | 0 |  | 
1 | 1 | 1 |  | 

## Slide 40: Single Bit Addition as a Truth Table
A | B | Cin | R | Cout
0 | 0 | 0 | 0 | 0
0 | 0 | 1 | 1 | 0
0 | 1 | 0 | 1 | 0
0 | 1 | 1 | 0 | 1
1 | 0 | 0 | 1 | 0
1 | 0 | 1 | 0 | 1
1 | 1 | 0 |  | 
1 | 1 | 1 |  | 

## Slide 41: Single Bit Addition as a Truth Table
A | B | Cin | R | Cout
0 | 0 | 0 | 0 | 0
0 | 0 | 1 | 1 | 0
0 | 1 | 0 | 1 | 0
0 | 1 | 1 | 0 | 1
1 | 0 | 0 | 1 | 0
1 | 0 | 1 | 0 | 1
1 | 1 | 0 | 0 | 1
1 | 1 | 1 |  | 

## Slide 42: Single Bit Addition as a Truth Table
A | B | Cin | R | Cout
0 | 0 | 0 | 0 | 0
0 | 0 | 1 | 1 | 0
0 | 1 | 0 | 1 | 0
0 | 1 | 1 | 0 | 1
1 | 0 | 0 | 1 | 0
1 | 0 | 1 | 0 | 1
1 | 1 | 0 | 0 | 1
1 | 1 | 1 | 1 | 1

## Slide 43: Single Bit Addition as a Formula

## Slide 44: Single Bit Addition as a
Formula
A | B | Cin | R | Cout
0 | 0 | 0 | 0 | 0
0 | 0 | 1 | 1 | 0
0 | 1 | 0 | 1 | 0
0 | 1 | 1 | 0 | 1
1 | 0 | 0 | 1 | 0
1 | 0 | 1 | 0 | 1
1 | 1 | 0 | 0 | 1
1 | 1 | 1 | 1 | 1
-If we take the truth table from before...

## Slide 45: Single Bit Addition as a
Formula
A | B | Cin | R | Cout
0 | 0 | 0 | 0 | 0
0 | 0 | 1 | 1 | 0
0 | 1 | 0 | 1 | 0
0 | 1 | 1 | 0 | 1
1 | 0 | 0 | 1 | 0
1 | 0 | 1 | 0 | 1
1 | 1 | 0 | 0 | 1
1 | 1 | 1 | 1 | 1
-Need a formula for each output
-Start with R (arbitrary; could also start at Cout)

## Slide 46: Single Bit Addition as a
Formula
A | B | Cin | R | Cout
0 | 0 | 0 | 0 | 0
0 | 0 | 1 | 1 | 0
0 | 1 | 0 | 1 | 0
0 | 1 | 1 | 0 | 1
1 | 0 | 0 | 1 | 0
1 | 0 | 1 | 0 | 1
1 | 1 | 0 | 0 | 1
1 | 1 | 1 | 1 | 1
-We have these products

## Slide 47: Single Bit Addition as a
Formula
A | B | Cin | R | Cout
0 | 0 | 0 | 0 | 0
0 | 0 | 1 | 1 | 0
0 | 1 | 0 | 1 | 0
0 | 1 | 1 | 0 | 1
1 | 0 | 0 | 1 | 0
1 | 0 | 1 | 0 | 1
1 | 1 | 0 | 0 | 1
1 | 1 | 1 | 1 | 1
R = !A!BCin +
!AB!Cin + A!B!Cin +
ABCin
-We have these products

## Slide 48: Single Bit Addition as a
Formula
A | B | Cin | R | Cout
0 | 0 | 0 | 0 | 0
0 | 0 | 1 | 1 | 0
0 | 1 | 0 | 1 | 0
0 | 1 | 1 | 0 | 1
1 | 0 | 0 | 1 | 0
1 | 0 | 1 | 0 | 1
1 | 1 | 0 | 0 | 1
1 | 1 | 1 | 1 | 1
R = !A!BCin +
!AB!Cin + A!B!Cin +
ABCin

## Slide 49: Single Bit Addition as a
Formula
A | B | Cin | R | Cout
0 | 0 | 0 | 0 | 0
0 | 0 | 1 | 1 | 0
0 | 1 | 0 | 1 | 0
0 | 1 | 1 | 0 | 1
1 | 0 | 0 | 1 | 0
1 | 0 | 1 | 0 | 1
1 | 1 | 0 | 0 | 1
1 | 1 | 1 | 1 | 1
R = !A!BCin +
!AB!Cin + A!B!Cin +
ABCin

## Slide 50: Single Bit Addition as a
Formula
A | B | Cin | R | Cout
0 | 0 | 0 | 0 | 0
0 | 0 | 1 | 1 | 0
0 | 1 | 0 | 1 | 0
0 | 1 | 1 | 0 | 1
1 | 0 | 0 | 1 | 0
1 | 0 | 1 | 0 | 1
1 | 1 | 0 | 0 | 1
1 | 1 | 1 | 1 | 1
R = !A!BCin +
!AB!Cin + A!B!Cin +
ABCin
Cout = !ABCin + A!BCin + AB!Cin +
ABCin

## Slide 51: Circuits

## Slide 52: Circuits
AND, OR, and NOT can be implemented with physical hardware
  Therefore, anything representable with AND, OR, and NOT can be turned into a hardware device

## Slide 53: AND Gate Circuit takes two inputs and produces one output

## Slide 54: AND Gate
Circuit takes two inputs and produces one output
AB

## Slide 55: AND Gate
A B
Circuit takes two inputs and produces one output
AB
Output (AB)

## Slide 56: OR Gate Circuit takes two inputs and produces one output

## Slide 57: OR Gate
Circuit takes two inputs and produces one output
A + B

## Slide 58: OR Gate
A B
Circuit takes two inputs and produces one output
A + B
Output (A + B)

## Slide 59: NOT (Inverter) Circuit takes one input and produces one output

## Slide 60: NOT (Inverter)
Circuit takes one input and produces one output
!A

## Slide 61: NOT (Inverter)
A
Circuit takes one input and produces one output
!A
Output(!A)

## Slide 62: Formula to Circuit

## Slide 63: Formula to Circuit
(AB)C

## Slide 64: Formula to Circuit
(AB)C
A B

## Slide 65: Formula to Circuit
(AB)C
A B
C

## Slide 66: Circuit to Formula

## Slide 67: Circuit to Formula
A
B C

## Slide 68: Circuit to Formula
A
B C
??? + ???

## Slide 69: Circuit to Formula
A
B C
!??? + ???

## Slide 70: Circuit to Formula
A
B C
!A + ???

## Slide 71: Circuit to Formula
A
B C
!A + (???)(???)

## Slide 72: Circuit to Formula
A
B C
!A + (B)(C)

## Slide 73: Circuit to Formula
A
B C
!A + BC