## Slide 1: COMP 122/L Lecture 19 Mahdi Ebrahimi Slides adapted from Dr. Kyle Dewey

## Slide 2: Overview
Circuit minimization
  Boolean algebra
  Karnaugh maps

## Slide 3: Circuit Minimization

## Slide 4: Motivation
Unnecessarily large programs: bad
Unnecessarily large circuits: Very Bad™
  Why?

## Slide 5: Motivation
Unnecessarily large programs: bad
Unnecessarily large circuits:Very Bad™
  Why?
    Bigger circuits = bigger chips = higher cost (non-linear too!)
    Longer circuits = more time needed to move electrons through = slower

## Slide 6: Simplification
Real-world formulas can often be simplified, according to algebraic rules
  How might we simplify the following?
R = AB + !AB
-How might we simplify this?

## Slide 7: Simplification
Real-world formulas can often be simplified, according to algebraic rules
  How might we simplify the following?
R = AB + !AB R = B(A + !A)
R = B(true) R = B

## Slide 8: Simplification Trick
Look for products that differ only in one variable
  One product has the original variable (A)
  The other product has the other variable (!A)
R = AB + !AB

## Slide 9: Additional Example 1
!ABCD + ABCD + !AB!CD + AB!CD

## Slide 10: Additional Example 1
!ABCD + ABCD + !AB!CD + AB!CD BCD(A + !A) + !AB!CD + AB!CD

## Slide 11: Additional Example 1
!ABCD + ABCD + !AB!CD + AB!CD BCD(A + !A) + !AB!CD + AB!CD BCD + !AB!CD + AB!CD

## Slide 12: Additional Example 1
!ABCD + ABCD + !AB!CD + AB!CD BCD(A + !A) + !AB!CD + AB!CD BCD + !AB!CD + AB!CD
BCD + B!CD(!A + A)

## Slide 13: Additional Example 1
!ABCD | + ABCD + !AB!CD | + | AB!CD
BCD(A BCD + | + !A) + !AB!CD !AB!CD + AB!CD | + | AB!CD
BCD + | B!CD(!A + A) |  | 
BCD + | B!CD |  | 

## Slide 14: Additional Example 1
!ABCD + ABCD + !AB!CD + AB!CD BCD(A + !A) + !AB!CD + AB!CD BCD + !AB!CD + AB!CD
BCD + B!CD(!A + A) BCD + B!CD
BD(C + !C)

## Slide 15: Additional Example 1
!ABCD + ABCD + !AB!CD + AB!CD BCD(A + !A) + !AB!CD + AB!CD BCD + !AB!CD + AB!CD
BCD + B!CD(!A + A) BCD + B!CD
BD(C + !C) BD

## Slide 16: Additional Example 2
!A!BC + A!B!C + !ABC + !AB!C + A!BC

## Slide 17: Additional Example 2
!A!BC + A!B!C + !ABC + !AB!C + A!BC
!A!BC + A!BC + A!B!C + !ABC + !AB!C

## Slide 18: Additional Example 2
!A!BC + A!B!C + !ABC + !AB!C + A!BC
!A!BC + A!BC + A!B!C + !ABC + !AB!C
!BC(A + !A) + A!B!C + !ABC + !AB!C

## Slide 19: Additional Example 2
!A!BC + A!B!C + !ABC + !AB!C + A!BC
!A!BC + A!BC + A!B!C + !ABC + !AB!C
!BC(A + !A) + A!B!C + !ABC + !AB!C
!BC + A!B!C + !ABC + !AB!C

## Slide 20: Additional Example 2
!A!BC + A!B!C + !ABC + !AB!C + A!BC
!A!BC + A!BC + A!B!C + !ABC + !AB!C
!BC(A + !A) + A!B!C + !ABC + !AB!C
!BC + A!B!C + !ABC + !AB!C
!BC + A!B!C + !AB(C + !C)

## Slide 21: Additional Example 2
!A!BC + A!B!C + !ABC + !AB!C + A!BC
!A!BC + A!BC + A!B!C + !ABC + !AB!C
!BC(A + !A) + A!B!C + !ABC + !AB!C
!BC + A!B!C + !ABC + !AB!C
!BC + A!B!C + !AB(C + !C)
!BC + A!B!C + !AB

## Slide 22
De Morgan’s Laws
Also potentially useful for simplification

## Slide 23: De Morgan’s Laws
Also potentially useful for simplification
!(A + B) = !A!B

## Slide 24: De Morgan’s Laws
Also potentially useful for simplification
!(A + B) = !A!B
!(AB) = !A + !B

## Slide 25
De Morgan Example
!(X + Y)!(!X + Z)

## Slide 26: De Morgan Example
!(X + Y)!(!X + Z)
!A !B
Has the overall form of !A!B

## Slide 27: De Morgan Example
!(X + Y)!(!X + Z)
!A !B
Has the overall form of !A!B

## Slide 28: De Morgan Example
!(X + Y)!(!X + Z)
!A !B
From De Morgan’s Law:
!(A + B) = !A!B
Has the overall form of !A!B

## Slide 29: De Morgan Example
!(X + Y)!(!X + Z)
!A !B
From De Morgan’s Law:
!(A + B) = !A!B
!(X + Y + !X + Z)
Has the overall form of !A!B

## Slide 30: De Morgan Example
!(X + Y)!(!X + Z)
!A !B
From De Morgan’s Law:
!(A + B) = !A!B
!(X + Y + !X + Z)
!(X + !X + Y + Z)
Has the overall form of !A!B

## Slide 31: De Morgan Example
!(X + Y)!(!X + Z)
!A !B
From De Morgan’s Law:
!(A + B) = !A!B
!(X + Y + !X + Z)
!(X + !X + Y + Z)
!(true + Y + Z)
Has the overall form of !A!B

## Slide 32: De Morgan Example
!(X + Y)!(!X + Z)
!A !B
From De Morgan’s Law:
!(A + B) = !A!B
!(X + Y + !X + Z)
!(X + !X + Y + Z)
!(true + Y + Z)
!(true)
Has the overall form of !A!B

## Slide 33: De Morgan Example
!(X + Y)!(!X + Z)
!A !B
From De Morgan’s Law:
!(A + B) = !A!B
!(X + Y + !X + Z)
!(X + !X + Y + Z)
!(true + Y + Z)
!(true) false
Has the overall form of !A!B

## Slide 34: Boolean Operators (Truth Table)
OR X + Y
AND X Y
Complement (opposite) X

## Slide 35: Boolean Algebra

## Slide 36: Scaling Up
Performing this sort of algebraic manipulation by hand can be tricky
We can use Karnaugh maps to make it immediately apparent as to what can be simplified
Karnaugh Maps - Rules of Simplification:
http://www.ee.surrey.ac.uk/Projects/Labview/minimisation/karrules.html

## Slide 37
Example
R = AB + !AB
-Start with the sum of products

## Slide 38: Example
R = AB + !AB
A | B | O
0 | 0 | 0
0 | 1 | 1
1 | 0 | 0
1 | 1 | 1
-Build the truth table

## Slide 39: Example
A | B | O
0 | 0 | 0
0 | 1 | 1
1 | 0 | 0
1 | 1 | 1
A
R = AB + !AB
B
0
1
0
1
0
0
1
1
-Build the K-map

## Slide 40: Example
A | B | O
0 | 0 | 0
0 | 1 | 1
1 | 0 | 0
1 | 1 | 1
A
R = AB + !AB
B
0
1
0
1
0
0
1
1
-Group adjacent (row or column-wise, NOT diagonal) 1’s in powers of two (groups of 2, 4, 8...)

## Slide 41: Example
A | B | O
0 | 0 | 0
0 | 1 | 1
1 | 0 | 0
1 | 1 | 1
A
R = AB + !AB
B
0
1
0
1
0
0
1
1
-The values that stay the same are saved, the rest are discarded
-This works because this means that the inputs that differ are irrelevant to the final value, and so they can be removed

## Slide 42: Example
A | B | O
0 | 0 | 0
0 | 1 | 1
1 | 0 | 0
1 | 1 | 1
A
0
1
0
1
0
0
1
1
R = AB + !AB
R = B
B
-The values that stay the same are saved, the rest are discarded
-This works because this means that the inputs that differ are irrelevant to the final value, and so they can be removed

## Slide 43: Three Variables
A
We can scale this up to three variables, by combining two variables on one axis
The combined axis must be arranged such that only one bit changes per position
BC
0
1
00 01
?
11
10
?
?
?
?
?
?
?

## Slide 44: Three Variable Example

## Slide 45: R = !A!BC + !ABC + A!BC + ABC
-Start with this formula

## Slide 46: R = !A!BC + !ABC + A!BC + ABC
A | B | C | R
0 0 0 |  |  | 0
0 0 1 |  |  | 1
0 1 0 |  |  | 0
0 1 1 |  |  | 1
1 0 0 |  |  | 0
1 0 1 |  |  | 1
1 1 0 |  |  | 0
1 1 1 |  |  | 1
-Build the truth table

## Slide 47: R = !A!BC + !ABC + A!BC + ABC
A | B | C | R
0 0 0 |  |  | 0
0 0 1 |  |  | 1
0 1 0 |  |  | 0
0 1 1 |  |  | 1
1 0 0 |  |  | 0
1 0 1 |  |  | 1
1 1 0 |  |  | 0
1 1 1 |  |  | 1
A
BC
0
1
00 01
0
11
10
0
1
1
1
1
0
0
-Build the K-map

## Slide 48: R = !A!BC + !ABC + A!BC + ABC
A | B | C | R
0 0 0 |  |  | 0
0 0 1 |  |  | 1
0 1 0 |  |  | 0
0 1 1 |  |  | 1
1 0 0 |  |  | 0
1 0 1 |  |  | 1
1 1 0 |  |  | 0
1 1 1 |  |  | 1
A
BC
0
00 01
0
11
10
1 0
1
1
1
0
1 0
-Select the biggest group possible, in this case a square
-In order to get the most minimal circuit, we must always select the biggest groups possible

## Slide 49: R = !A!BC + !ABC + A!BC + ABC
A | B | C | R
0 0 0 |  |  | 0
0 0 1 |  |  | 1
0 1 0 |  |  | 0
0 1 1 |  |  | 1
1 0 0 |  |  | 0
1 0 1 |  |  | 1
1 1 0 |  |  | 0
1 1 1 |  |  | 1
A
0
00 01
0
11
10
1 0
1
1
1
1
0
0
R = C
BC
-Save the ones that stay the same in a group, discarding the rest

## Slide 50: Another Three Variable Example

## Slide 51
R = | !A!B!C | + !A!BC | + !ABC | +
 | !AB!C + | A!B!C + | AB!C | 
-Start with this formula

## Slide 52
A | B | C | R
0 0 0 |  |  | 1
0 0 1 |  |  | 1
0 1 0 |  |  | 1
0 1 1 |  |  | 1
1 0 0 |  |  | 1
1 0 1 |  |  | 0
1 1 0 |  |  | 1
1 1 1 |  |  | 0
R = | !A!B!C | + !A!BC | + !ABC | +
 | !AB!C + | A!B!C + | AB!C | 
-Build the truth table

## Slide 53
A
BC
0
1
00 01
1
11
10
1
1
0
1
0
1
1
R = | !A!B!C | + !A!BC | + !ABC | +
 | !AB!C + | A!B!C + | AB!C | 
A | B | C | R
0 0 0 |  |  | 1
0 0 1 |  |  | 1
0 1 0 |  |  | 1
0 1 1 |  |  | 1
1 0 0 |  |  | 1
1 0 1 |  |  | 0
1 1 0 |  |  | 1
1 1 1 |  |  | 0
-Build the K-map

## Slide 54
A
BC
0
1
00 01
11
10
R = | !A!B!C | + !A!BC | + !ABC | +
 | !AB!C + | A!B!C + | AB!C | 
A | B | C | R
0 0 0 |  |  | 1
0 0 1 |  |  | 1
0 1 0 |  |  | 1
0 1 1 |  |  | 1
1 0 0 |  |  | 1
1 0 1 |  |  | 0
1 1 0 |  |  | 1
1 1 1 |  |  | 0
 | 1 | 1 1 | 1 | 
1 |  | 0 0 | 1 | 
-Select the biggest groups possible
-Note that the values “wrap around” the table

## Slide 55
A
BC
0
1
00 01
11
10
R = | !A!B!C | + !A!BC | + !ABC | +
 | !AB!C + | A!B!C + | AB!C | 
A | B | C | R
0 0 0 |  |  | 1
0 0 1 |  |  | 1
0 1 0 |  |  | 1
0 1 1 |  |  | 1
1 0 0 |  |  | 1
1 0 1 |  |  | 0
1 1 0 |  |  | 1
1 1 1 |  |  | 0
 | 1 | 1 1 | 1 | 
1 |  | 0 0 | 1 | 
-Save the ones that stay the same in a group, discarding the rest
-This must be done for each group

## Slide 56
A
BC
0
1
00 01
11
10
R = | !A!B!C | + !A!BC | + !ABC | +
 | !AB!C + | A!B!C + | AB!C | 
A | B | C | R
0 0 0 |  |  | 1
0 0 1 |  |  | 1
0 1 0 |  |  | 1
0 1 1 |  |  | 1
1 0 0 |  |  | 1
1 0 1 |  |  | 0
1 1 0 |  |  | 1
1 1 1 |  |  | 0
 | 1 | 1 1 | 1 | 
1 |  | 0 0 | 1 | 
-Save the ones that stay the same in a group, discarding the rest
-This must be done for each group

## Slide 57: R =!A + !C
A
BC
0
1
00 01
11
10
R = | !A!B!C | + !A!BC | + !ABC | +
 | !AB!C + | A!B!C + | AB!C | 
A | B | C | R
0 0 0 |  |  | 1
0 0 1 |  |  | 1
0 1 0 |  |  | 1
0 1 1 |  |  | 1
1 0 0 |  |  | 1
1 0 1 |  |  | 0
1 1 0 |  |  | 1
1 1 1 |  |  | 0
 | 1 | 1 1 | 1 | 
1 |  | 0 0 | 1 | 
-Save the ones that stay the same in a group, discarding the rest
-This must be done for each group

## Slide 58: Four Variable Example

## Slide 59: R = !A!B!C!D + !A!B!CD + !A!BC!D + !ABC!D + A!B!C!D + A!B!CD + A!BC!D
-Take this formula

## Slide 60: R = !A!B!C!D + !A!B!CD + !A!BC!D + !ABC!D + A!B!C!D + A!B!CD + A!BC!D
AB
CD
00 01
11
10
1
1
0
1
00
01
11
0
0
1
0
0
10 1
0
0
0
1
0
1
-For space reasons, we go directly to the K-map

## Slide 61: R = !A!B!C!D + !A!B!CD + !A!BC!D + !ABC!D + A!B!C!D + A!B!CD + A!BC!D
AB
CD
00 01
11
10
1
1
0
1
1
00
01
11
10
0
0
1
0
0
1
0
0
0
0
1
-Group things up
-The edges logically wrap around!
-Groups may overlap each other

## Slide 62: R = !A!B!C!D + !A!B!CD + !A!BC!D + !ABC!D + A!B!C!D + A!B!CD + A!BC!D
AB
CD
00
10
1
1
1
00
01
11
10
0
0
1
0
0
1
0
0
0
0
1
R =!B!C
01 11
1 0
-Look at the bits that don’t change
-First for the cube

## Slide 63: R = !A!B!C!D + !A!B!CD + !A!BC!D + !ABC!D + A!B!C!D + A!B!CD + A!BC!D
AB
CD
00
1
0
00
01
11
10
0
0
1
0
0
1
0
0
0
R =!B!C + !B!D
01 11 10
1 1
1
0
1
-Look at the bits that don’t change
-Second for the cube on the edges

## Slide 64: R = !A!B!C!D + !A!B!CD + !A!BC!D + !ABC!D + A!B!C!D + A!B!CD + A!BC!D
AB
CD
0
1 1 1
1
00
01
11
10
0
0
1
0
0
1
0
0
0
0
1
R =!B!C + !B!D + !AC!D
00 01 11 10
-Look at the bits that don’t change
-Third for the line

## Slide 65: K-Map Rules in Summary (1)
Groups can contain only 1s
Only 1s in adjacent groups are allowed (no diagonals)
The number of 1s in a group must be a power of two (1, 2, 4, 8...)
The groups must be as large as legally possible

## Slide 66: K-Map Rules in Summary (2)
All 1s must belong to a group, even if it’s a group of one element
Overlapping groups are permitted
Wrapping around the map is permitted
Use the fewest number of groups possible

## Slide 67
Revisiting Problem
!A!BC + A!B!C + !ABC + !AB!C + A!BC

## Slide 68: Revisiting Problem R = !A!BC + A!B!C + !ABC + !AB!C + A!BC
A | B | C | R
0 0 0 |  |  | 0
0 0 1 |  |  | 1
0 1 0 |  |  | 1
0 1 1 |  |  | 1
1 0 0 |  |  | 1
1 0 1 |  |  | 1
1 1 0 |  |  | 0
1 1 1 |  |  | 0

## Slide 69: Revisiting Problem R = !A!BC + A!B!C + !ABC + !AB!C + A!BC
A
BC
0
1
00 01
0
11
10
1
1
1
1
0
1
0
A | B | C | R
0 0 0 |  |  | 0
0 0 1 |  |  | 1
0 1 0 |  |  | 1
0 1 1 |  |  | 1
1 0 0 |  |  | 1
1 0 1 |  |  | 1
1 1 0 |  |  | 0
1 1 1 |  |  | 0

## Slide 70: Revisiting Problem R = !A!BC + A!B!C + !ABC + !AB!C + A!BC
A
0
1
00
0
01 11
10
1
1 1
1 0
1
0
A | B | C | R
0 0 0 |  |  | 0
0 0 1 |  |  | 1
0 1 0 |  |  | 1
0 1 1 |  |  | 1
1 0 0 |  |  | 1
1 0 1 |  |  | 1
1 1 0 |  |  | 0
1 1 1 |  |  | 0
R = !AC
BC

## Slide 71: Revisiting Problem R = !A!BC + A!B!C + !ABC + !AB!C + A!BC
A
0
1
00
0
01 11
10
1
1 1
1 0
1
0
A | B | C | R
0 0 0 |  |  | 0
0 0 1 |  |  | 1
0 1 0 |  |  | 1
0 1 1 |  |  | 1
1 0 0 |  |  | 1
1 0 1 |  |  | 1
1 1 0 |  |  | 0
1 1 1 |  |  | 0
R = !AC + A!B
BC

## Slide 72: Revisiting Problem R = !A!BC + A!B!C + !ABC + !AB!C + A!BC
A
0
1
00
0
01 11
10
1
1 1
1 0
1
0
A | B | C | R
0 0 0 |  |  | 0
0 0 1 |  |  | 1
0 1 0 |  |  | 1
0 1 1 |  |  | 1
1 0 0 |  |  | 1
1 0 1 |  |  | 1
1 1 0 |  |  | 0
1 1 1 |  |  | 0
R = !AC + A!B + !AB!C
BC

## Slide 73: Difference
Algebraic solution: !BC + A!B!C + !AB
K-map solution: !AC + A!B + !AB!C
Question: why might these differ?

## Slide 74: Difference
Algebraic solution: !BC + A!B!C + !AB
K-map solution: !AC + A!B + !AB!C
Question: why might these differ?
  Both are minimal, in that they have the fewest number of products possible
  Can be multiple minimal solutions

## Slide 75: Difference
A
BC
0
1
00
0
01 11
10
1
1 1
1 0
1
0
Algebraic solution: !BC | + | A!B!C | + !AB
K-map solution: !AC | + | A!B + | !AB!C
-If we take our k-map from before with the grouping we chose, we get this particular solution

## Slide 76: Difference
A
BC
0
1
00 01
0
11
10
1
1
1
1
0
1
0
Algebraic solution: !BC + A!B!C + !AB
K-map solution: !BC + A!B!C + !AB
-If, however, we choose a different (also valid) grouping, we get the same solution as we did algebraically

## Slide 77: Don’t Cares
Don’t cares in a Karnaugh map, or truth table, may be either 1s or 0s, as long as we don’t care what the output is for an input condition we never expect to see. We plot these cells with an asterisk, *, among the normal 1s and 0s.
When forming groups of cells, treat the don’t care cell as either a 1 or a 0, or ignore the don’t cares.
This is helpful if it allows us to form a larger group than would otherwise be possible without the don’t cares. There is no requirement to group all or any of the don’t cares.
Only use them in a group if it simplifies the logic.

## Slide 78
A
BC
0
1
00 01
0
11
10
0
X
X
X
0
0
1