## Slide 1: Number Systems and Number Representation
1

## Slide 2: Goals of this Lecture
Help you learn (or refresh your memory) about:
The binary, hexadecimal, and octal number systems
Finite representation of unsigned integers
Finite representation of signed integers
Finite representation of rational numbers (if time)
Why?
A power programmer must know number systems and data representation to fully understand C’s primitive data types
Primitive values and the operations on them

## Slide 3: Agenda
Number Systems
Finite representation of unsigned integers Finite representation of signed integers
Finite representation of rational numbers (if time)

## Slide 4: The Decimal Number System
Name
“decem” (Latin) => ten
Characteristics
Ten symbols
  0 1 2 3 4 5 6 7 8 9
Positional
  2945 ≠ 2495
  2945 = (2*103) + (9*102) + (4*101) + (5*100)
(Most) people use the decimal number system

## Slide 5: The Binary Number System
Name
“binarius” (Latin) => two
Characteristics
Two symbols
  0 1
Positional
  1010B ≠ 1100B
Most (digital) computers use the binary number system
Terminology
Bit: a binary digit
Byte: (typically) 8 bits

## Slide 6: Decimal-Binary Equivalence
Decimal | Binary |  | Decimal Binary
0 | 0 |  | 16 10000
1 | 1 |  | 17 10001
2 | 10 |  | 18 10010
3 | 11 |  | 19 10011
4 | 100 |  | 20 10100
5 | 101 |  | 21 10101
6 | 110 |  | 22 10110
7 | 111 |  | 23 10111
8 | 1000 |  | 24 11000
9 | 1001 |  | 25 11001
10 | 1010 |  | 26 11010
11 | 1011 |  | 27 11011
12 | 1100 |  | 28 11100
13 | 1101 |  | 29 11101
14 | 1110 |  | 30 11110
15 | 1111 |  | 31 11111
 |  |  | ... ...

## Slide 7: Decimal-Binary Conversion
Binary to decimal: expand using positional notation
(1*25)+(0*24)+(0*23)+(1*22)+
100101B = = | (1*25)+(0*24)+(0*23)+(1*22)+(0*21)+(1*20) 32 + 0 + 0 + 4 + 0 + 1 |  |  |  |  |  |  |  |  |  | 
= | 37 |  |  |  |  |  |  |  |  |  | 

## Slide 8: Decimal-Binary Conversion
Decimal to binary: do the reverse
Determine largest power of 2 ≤ number; write template
Fill in template
37 = (?*25)+(?*24)+(?*23)+(?*22)+(?*21)+(?*20)
37 = (1*25)+(0*24)+(0*23)+(1*22)+(0*21)+(1*20)
-32
5
-4
1 100101B
-1
0

## Slide 9: Decimal-Binary Conversion
Decimal to binary shortcut
Repeatedly divide by 2, consider remainder
37 / 2 = 18 R 1
18 / 2 = 9 R 0
9 / 2 = 4 R 1
4 / 2 = 2 R 0
2 / 2 = 1 R 0
1 / 2 = 0 R 1
Read from bottom to top: 100101B

## Slide 10: The Hexadecimal Number System
Name
“hexa” (Greek) => six
“decem” (Latin) => ten
Characteristics
Sixteen symbols
  0 1 2 3 4 5 6 7 8 9 A B C D E F
Positional
  A13DH ≠ 3DA1H
Computer programmers often use the hexadecimal number
system

## Slide 11: Decimal-Hexadecimal Equivalence
Decimal | Hex |  | Decimal Hex |  | Decimal | Hex
0 | 0 |  | 16 10 |  | 32 | 20
1 | 1 |  | 17 11 |  | 33 | 21
2 | 2 |  | 18 12 |  | 34 | 22
3 | 3 |  | 19 13 |  | 35 | 23
4 | 4 |  | 20 14 |  | 36 | 24
5 | 5 |  | 21 15 |  | 37 | 25
6 | 6 |  | 22 16 |  | 38 | 26
7 | 7 |  | 23 17 |  | 39 | 27
8 | 8 |  | 24 18 |  | 40 | 28
9 | 9 |  | 25 19 |  | 41 | 29
10 | A |  | 26 1A |  | 42 | 2A
11 | B |  | 27 1B |  | 43 | 2B
12 | C |  | 28 1C |  | 44 | 2C
13 | D |  | 29 1D |  | 45 | 2D
14 | E |  | 30 1E |  | 46 | 2E
15 | F |  | 31 1F |  | 47 | 2F
 |  |  |  |  | ... | ...

## Slide 12: Decimal-Hexadecimal Conversion
Hexadecimal to decimal: expand using positional notation
Decimal to hexadecimal: use the shortcut
25H = (2*161) + = 32 + |  |  | (5*160) 5
= | 37 |  | 
37 / 16 = 2 R 5
2 / 16 = 0 R 2
Read from bottom to top: 25H

## Slide 13: Binary-Hexadecimal Conversion
Observation: 161 = 24
Every 1 hexadecimal digit corresponds to 4 binary digits
Binary to hexadecimal
1010000100111101B A 1 3 DH
Digit count in binary number not a multiple of 4 =>
pad with zeros on left
Hexadecimal to binary
A 1 3 DH 1010000100111101B
Discard leading zeros from binary number if appropriate

## Slide 14: The Octal Number System
Name
“octo” (Latin) => eight
Characteristics
Eight symbols
  0 1 2 3 4 5 6 7
Positional
  1743O ≠ 7314O
Computer programmers often use the octal number system

## Slide 15: Decimal-Octal Equivalence
Decimal | Octal |  | Decimal Octal |  | Decimal | Octal
0 | 0 |  | 16 20 |  | 32 | 40
1 | 1 |  | 17 21 |  | 33 | 41
2 | 2 |  | 18 22 |  | 34 | 42
3 | 3 |  | 19 23 |  | 35 | 43
4 | 4 |  | 20 24 |  | 36 | 44
5 | 5 |  | 21 25 |  | 37 | 45
6 | 6 |  | 22 26 |  | 38 | 46
7 | 7 |  | 23 27 |  | 39 | 47
8 | 10 |  | 24 30 |  | 40 | 50
9 | 11 |  | 25 31 |  | 41 | 51
10 | 12 |  | 26 32 |  | 42 | 52
11 | 13 |  | 27 33 |  | 43 | 53
12 | 14 |  | 28 34 |  | 44 | 54
13 | 15 |  | 29 35 |  | 45 | 55
14 | 16 |  | 30 36 |  | 46 | 56
15 | 17 |  | 31 37 |  | 47 | 57
 |  |  |  |  | ... | ...

## Slide 16: Decimal-Octal Conversion
Octal to decimal: expand using positional notation
Decimal to octal: use the shortcut
37O = (3*81) + (7*80) = 24 + 7 |  |  | 
= | 31 |  | 
31 / 8 = 3 R 7
3 / 8 = 0 R 3
Read from bottom to top: 37O

## Slide 17: Binary-Octal Conversion
Observation: 81 = 23
Every 1 octal digit corresponds to 3 binary digits
Binary to octal
001010000100111101B
1 2 0 4 7 5O
Digit count in binary number not a multiple of 3 =>
pad with zeros on left
Discard leading zeros from binary number if appropriate
Octal to binary
1 2 0 4 7 5O
001010000100111101B

## Slide 18: Agenda
Number Systems
Finite representation of unsigned integers
Finite representation of signed integers
Finite representation of rational numbers (if time)

## Slide 19: Unsigned Data Types: Java vs. C
Java has type
int
  Can represent signed integers
C has type:
signed int
  Can represent signed integers
int
  Same as signed int
unsigned int
  Can represent only unsigned integers
To understand C, must consider representation of both unsigned and signed integers

## Slide 20: Representing Unsigned Integers
Mathematics
Range is 0 to ∞
Computer programming
Range limited by computer’s word size
Word size is n bits => range is 0 to 2n – 1
Exceed range => overflow
Nobel computers with gcc217
n = 32, so range is 0 to 232 – 1 (4,294,967,295)
Pretend computer
n = 4, so range is 0 to 24 – 1 (15)
Hereafter, assume word size = 4
All points generalize to word size = 32, word size = n

## Slide 21: Representing Unsigned Integers
On pretend computer
Unsigned Integer | Rep
0 | 0000
1 | 0001
2 | 0010
3 | 0011
4 | 0100
5 | 0101
6 | 0110
7 | 0111
8 | 1000
9 | 1001
10 | 1010
11 | 1011
12 | 1100
13 | 1101
14 | 1110
15 | 1111

## Slide 22: Adding Unsigned Integers
Addition
Results are mod 24
7
+ 10
11
0111B
+ 1010B
1
10001B
1 3 0011B |  |  | 
+ | 10 -- | + | 1010B ----
 | 13 |  | 1101B
Start at right column Proceed leftward
Carry 1 when necessary
Beware of overflow

## Slide 23: Subtracting Unsigned Integers
Subtraction
3
- 10
2
0011B
- 1010B
9 1001B
Results are mod 24
10
- 7
12
0202
1010B
- 0111B
3
0011B
Start at right column Proceed leftward
Borrow 2 when necessary
Beware of overflow

## Slide 24: Shifting Unsigned Integers
Results are mod 24
5 << 1 => 10
3 << 2 => 12
Bitwise right shift (>>): fill on left with zeros
What is the effect arithmetically? (No fair looking ahead)
Bitwise left shift (<<): fill on right with zeros
What is the effect arithmetically? (No fair looking ahead)
10 >> | 1 | => 5
1010B |  | 0101B
10 >> | 2 | => 2
1010B |  | 0010B
0101B 1010B
0011B 1100B

## Slide 25: Shift Left as Multiplication
Equivalent decimal operation:
234

## Slide 26
Equivalent decimal operation:
234 << 1 =
2340
Shift Left as Multiplication

## Slide 27: Shift Left as Multiplication
Equivalent decimal operation:
234 << 1 =
2340
234 << 2 =
23400

## Slide 28: Multiplication
Shifting left N positions multiplies by
(base)N
Multiplying by 2 or 4 is often necessary (shift left 1 or 2 positions, respectively)
Often a whooole lot faster than telling the processor to multiply
234 << 2 =
23400

## Slide 29: Shift Right as Division
Question: If shifting left multiplies, what does shift right do?
  Answer: divides in a similar way, but truncates result

## Slide 30: Shift Right as Division
Question: If shifting left multiplies, what does shift right do?
  Answer: divides in a similar way, but truncates result
234

## Slide 31: Shift Right as Division
Question: If shifting left multiplies, what does shift right do?
  Answer: divides in a similar way, but
truncates result
234 >> 1 =
23

## Slide 32: Other Operations on Unsigned Ints
Bitwise NOT (~)
Flip each bit
~10 => 5
10
& 7
--
2
1010B & 0111B
----
0010B
Useful for setting selected bits to 0
1010B 0101B
Bitwise AND (&)
Logical AND corresponding bits

## Slide 33: Other Operations on Unsigned Ints
Bitwise OR: (|)
Logical OR corresponding bits
Bitwise exclusive OR (^)
Logical exclusive OR corresponding bits
10
| 1
--
11
1010B
| 0001B
----
1011B
Useful for setting selected bits to 1
10
^ 10
--
0
1010B
^ 1010B
----
0000B
x ^ x sets all bits to 0
The binary XOR operation will always produce a 1 output if either of its inputs is 1 and will produce a 0 output if both of its inputs are 0 or 1.

## Slide 34: Aside: Using Bitwise Ops for Arith
Can use <<, >>, and & to do some arithmetic efficiently
x * 2y == x << y
3*4 = 3*22 = 3 << 2 => 12
x / 2y == x >> y
13/4 = 13/22 = 13 >> 2 => 3
x % 2y == x & (2y-1)
13%4 = 13%22 = 13&(22-1)
= 13&3 => 1
Fast way to multiply
by a power of 2
Fast way to divide
by a power of 2
Fast way to mod
by a power of 2
13
& 3
1101B & 0011B
1
0001B
0011B
1100B
1101B
0011B

## Slide 35: Agenda
Number Systems
Finite representation of unsigned integers
Finite representation of signed integers
Finite representation of rational numbers (if time)

## Slide 36: Signed Magnitude
Integer | Rep
-7 | 1111
-6 | 1110
-5 | 1101
-4 | 1100
-3 | 1011
-2 | 1010
-1 | 1001
-0 | 1000
0 | 0000
1 | 0001
2 | 0010
3 | 0011
4 | 0100
5 | 0101
6 | 0110
7 | 0111
Definition
High-order bit indicates sign 0 => positive
1 => negative
Remaining bits indicate magnitude
B B
1101 = -101 = -5
0101B
= 101B = 5

## Slide 37: Signed Magnitude (cont.)
Integer | Rep
-7 | 1111
-6 | 1110
-5 | 1101
-4 | 1100
-3 | 1011
-2 | 1010
-1 | 1001
-0 | 1000
0 | 0000
1 | 0001
2 | 0010
3 | 0011
4
5
6
7
0100
0101
0110
0111
Computing negative
neg(x) = flip high order bit of x neg(0101B) = 1101B neg(1101B) = 0101B
Pros and cons
+ easy for people to understand
+ symmetric
- two reps of zero
- one of the bit patterns is wasted.
- addition doesn't work the way we want it to.
Notes: ADVANTAGE of signed magnitude: You can determine whether a number is negative or non negative simply by testing the most significant bit.
DISADVANTAGES of signed magnitude: One of the bit patterns is wasted. Addition doesn't work the way we want it to.

## Slide 38: Signed Magnitude (cont.)
Problem #1: "The Case of the Missing Bit Pattern":
How many possible bit patterns can be created with 4 bits?
Easy, we know that's 16. In unsigned representation, we were able to represent 16 numbers: 0, 1, 2, 3, 4, 5, 6, 7, 8, 9, 10, 11, 12, 13, 14, and 15.
But with signed magnitude, we are only able to represent 15 numbers: -7, -6, -5, -4, -3, -2, -1, 0, 1, 2, 3, 4, 5, 6, and 7.
There's still 16 bit patterns, but one of them is either not being used or is duplicating a number. That bit pattern is '1000B’.
When we interpret this pattern, we get '-0' which is both nonsensical (negative zero? come on!) and redundant (we already have '0000B' to represent 0).
Notes: ADVANTAGE of signed magnitude: You can determine whether a number is negative or non negative simply by testing the most significant bit.
DISADVANTAGES of signed magnitude: One of the bit patterns is wasted. Addition doesn't work the way we want it to.

## Slide 39: Signed Magnitude (cont.)
Problem #2: "Requires Special Care and Feeding": Remember we wanted to
have negative binary numbers so we could use our binary addition algorithm to
simulate binary subtraction. How does signed magnitude fare with addition? To
test it, let's try subtracting 2 from 5 by adding 5 and -2. A positive 5 would be
represented with the bit pattern '0101B' and -2 with '1010B'. Let's add these two
numbers and see what the result is:
Now we interpret the result as a signed magnitude number. The sign is '0' (non-
negative) and the magnitude is '7'. So the answer is a positive 7. But, wait a
minute, 5-2=3! This obviously didn't work.
Conclusion: signed magnitude doesn't work with regular binary addition
algorithms.
Notes: ADVANTAGE of signed magnitude: You can determine whether a number is negative or non negative simply by testing the most significant bit.
DISADVANTAGES of signed magnitude: One of the bit patterns is wasted. Addition doesn't work the way we want it to.

## Slide 40: Ones’ Complement
Integer | Rep
-7 | 1000
-6 | 1001
-5 | 1010
-4 | 1011
-3 | 1100
-2 | 1101
-1 | 1110
-0 | 1111
0 | 0000
1 | 0001
2 | 0010
3 | 0011
4
5
6
7
0100
0101
0110
0111
Definition
High-order bit has weight -7 (- 2n + 1 )
B
0010B
1010 = (1*-7)+(0*4)+(1*2)+(0*1)
= -5
= (0*-7)+(0*4)+(1*2)+(0*1)
= 2

## Slide 41: Ones’ Complement (cont.)
7
0111
- two reps of zero
Integer | Rep
-7 | 1000
-6 | 1001
-5 | 1010
-4 | 1011
-3 | 1100
-2 | 1101
-1 | 1110
-0 | 1111
0 | 0000
1 | 0001
2 | 0010
3 | 0011
4 | 0100
5 | 0101
6 | 0110
Computing negative
neg(x) = ~x
neg(0101 ) = 1010
B B
Pros and cons
+ symmetric
neg(1010B) = 0101B
Computing negative (alternative)
neg(x) = 1111B - x
neg(0101 ) = 1111 – 0101
B B B
= 1010B
neg(1010B) = 1111B – 1010B
= 0101
B

## Slide 42: Two’s Complement
35
Integer | Rep
-8 | 1000
-7 | 1001
-6 | 1010
-5 | 1011
-4 | 1100
-3 | 1101
-2 | 1110
-1 | 1111
0 | 0000
1 | 0001
2 | 0010
3 | 0011
4 | 0100
5 | 0101
6 | 0110
7 | 0111
Definition
High-order bit has weight -8 (-2n)
B
0010B
1010 = (1*-8)+(0*4)+(1*2)+(0*1)
= -6
= (0*-8)+(0*4)+(1*2)+(0*1)
= 2

## Slide 43: Two’s Complement (cont.)
Integer | Rep
-8 | 1000
-7 | 1001
-6 | 1010
-5 | 1011
-4 | 1100
-3 | 1101
-2 | 1110
-1 | 1111
0 | 0000
1 | 0001
2 | 0010
3 | 0011
4 | 0100
5 | 0101
6 | 0110
7 | 0111
Computing negative
neg(x) = ~x + 1
neg(x) = onescomp(x) + 1
neg(0101B) | = | 1010B | + | 1 | = | 1011B
neg(1011B) | = | 0100B | + | 1 | = | 0101B
Pros and cons
- not symmetric
+ one rep of zero

## Slide 44: Two’s Complement (cont.)
Almost all computers use two’s complement to represent signed integers
Why?
Arithmetic is easy
  Will become clear soon
Hereafter, assume two’s complement representation of signed integers

## Slide 45: Adding Signed Integers
38
3
+ 3
11
0011B
+ 0011B
7
+ 1
111
0111B
+ 0001B
-8
1000B
pos + pos pos + pos (overflow)
3
+ -1
1111
0011B
+ 1111B
6 0110B
pos + neg
-3
+ -2
11
1101B
+ 1110B
-5
11011B
2 10010B
neg + neg
-6
+ -5
1 1
1010B
+ 1011B
5
10101B
neg + neg (overflow)

## Slide 46: Subtracting Signed Integers
 | 1 |  |  |  | 
 | 22 |  |  |  | 
3 | 0011B |  |  | 3 | 0011B
- 4 | - 0100B |  | + | -4 | + 1100B
-1 | 1111B |  |  | -1 | 1111B
 |  |  |  | 111 | 
-5 | 1011B |  |  | -5 | 1011
- 2 | - 0010B |  | + | -2 | + 1110
-7 | 1001B |  |  | -7 | 11001
Perform subtraction with borrows
Compute two’s comp and add
or

## Slide 47: Negating Signed Ints: Math
Question: Why does two’s comp arithmetic work?
Answer: [–b] mod 24 = [twoscomp(b)] mod 24
See Bryant & O’Hallaron book for much more info
[–b] mod 24
= [24 – b] mod 24
= [24 – 1 - b + 1] mod 24
= [(24 – 1 - b) + 1] mod 24
= [onescomp(b) + 1] mod 24
= [twoscomp(b)] mod 24

## Slide 48: Subtracting Signed Ints: Math
And so:
[a – b] mod 24 = [a + twoscomp(b)] mod 24
See Bryant & O’Hallaron book for much more info
[a – b] mod 24
= [a + 24 – b] mod 24
= [a + 24 – 1 – b + 1] mod 24
= [a + (24 - 1 – b) + 1] mod 24
= [a + onescomp(b) + 1] mod 24
= [a + twoscomp(b)] mod 24

## Slide 49: Shifting Signed Integers
Bitwise (logical/arithmetic) left shift (<<): fill on right with zeros
Bitwise arithmetic right shift: fill on left with sign bit
Results are mod 24
6 >> 1 => 3
-6 >> 1 => -3
3 << 1 => 6
-3 << 1 => -6
0011B 0110B
1101B 1010B
0110B 0011B
1010B 1101B
Shift by n = multiplying by 2n
Shift by n = dividing by 2n
and Round-floor

## Slide 50: Shifting Signed Integers (cont.)
Bitwise logical right shift: fill on left with zeros
Right shift (>>) could be logical or arithmetic
Compiler designer decides
Logical shift is ideal for unsigned binary numbers
Arithmetic shift is ideal for signed two’s complement binary numbers
6 >> 1 => 3
-6 >> 1 => 5
0110B 0011B
1010B 0101B
?

## Slide 51: Other Operations on Signed Ints
Bitwise NOT (~)
Same as with unsigned ints
Bitwise AND (&)
Same as with unsigned ints
Bitwise OR: (|)
Same as with unsigned ints
Bitwise exclusive OR (^)
Same as with unsigned ints

## Slide 52: Agenda
Number Systems
Finite representation of unsigned integers Finite representation of signed integers
Finite representation of rational numbers (if time)

## Slide 53: Number Systems
So far, we have studied the following integer number systems in computer
  Unsigned numbers
  Sign/magnitude numbers
  Two’s complement numbers
What about rational numbers?
A rational number is one that can be expressed as the ratio of two integers
Infinite range and precision
For example, 2.5, -10.04, 0.75 etc

## Slide 54: Rational Numbers
Computer science
Finite range and precision
Approximate using floating point number
  Binary point “floats” across bits
Two common notations to represent rational numbers in computer
  Fixed-point numbers
  Floating-point numbers

## Slide 55: Fixed-Point Numbers
Fixed point notation has an implied binary point between the integer and fraction bits
  The binary point is not a part of the representation but is implied
  Example:
    Fixed-point representation of 6.75 using 4 integer bits and 4 fraction bits:
The number of integer and fraction bits must be agreed upon by those generating and those reading the number
  There is no way of knowing the existence of the binary point except through agreement of those people interpreting the number

## Slide 56: Signed Fixed-Point Numbers
As with whole numbers, negative fractional numbers can be represented in two ways
  Sign/magnitude notation
  Two’s complement notation
Example:
  -2.375 using 8 bits (4 bits each to represent integer and fractional parts)
    2.375 = 0010 . 0110
    Sign/magnitude notation: 1010 0110
    Two’s complement notation:
  1. flip all the bits: 1101 1001
  2. add 1: + 1
  1101 1010
Addition and subtraction works easily in computer with 2’s complement notation like integer addition and subtraction

## Slide 57: Example
Suppose that we have 8 bits to represent a number
  4 bits for integer and 4 bits for fraction
Compute 0.75 + (-0.625)
  0.75 = 0000 1100
  0.625 = 0000 1010
  -0.625 in 2’s complement form: 1111 0110
  0.75 0000 1100
  + - 0.625 1111 0110
  0000 0010
0.125

## Slide 58: Fixed-Point Number Systems
Fixed-point number systems have a limitation of having a constant number of integer and fractional bits
Some low-end digital signal processors support fixed-point numbers
  Example: TMS320C550x TI (Texas Instruments) DSPs: www.ti.com

## Slide 59: Floating-Point Numbers
Floating-point number systems circumvent the limitation of having a constant number of integer and fractional bits
  They allow the representation of very large and very small numbers
The binary point floats to the right of the most significant 1
  Similar to decimal scientific notation
  For example, write 27310 in scientific notation:
    Move the decimal point to the right of the most significant digit and increase the exponent:
  273 = 2.73 × 102
In general, a number is written in scientific notation as:
± M × BE
Where,
  M = mantissa
  B = base
  E = exponent
  In the example, M = 2.73, B = 10, and E = 2 (that is, +2.73 × 102)

## Slide 60: Floating-Point Numbers
Floating-point number representation using 32 bits
  1 sign bit
  8 exponent bits
  23 bits for the mantissa.
The following slides show three versions of floating-point representation with 22810 using a 32-bit
  The final version is called the IEEE 754 floating-point standard

## Slide 61: Floating-Point Representation #1
First, convert the decimal number to binary
  22810 = 111001002 = 1.11001 × 27
Next, fill in each field in the 32-bit:
  The sign bit (1 bit) is positive, so 0
  The exponent (8 bits) is 7 (111)
  The mantissa (23 bits) is 1.11001
/ Fraction

## Slide 62: Floating-Point Representation #2
You may have noticed that the first bit of the mantissa is always 1, since the binary point floats to the right of the most significant 1
  Example: 22810 = 111001002 = 1.11001 × 27
Thus, storing the most significant 1 (also called the implicit leading 1) is redundant information
We can store just the fraction parts in the 23-bit field
  Now, the leading 1 is implied
0 0 0 0 0 1 1 1
Mantissa /

## Slide 63: Floating-Point Representation #3
  The exponent needs to represent both positive and negative
The final change is to use a biased exponent
  The IEEE 754 standard uses a bias of 127
  Biased exponent = bias + exponent
    For example, an exponent of 7 is stored as 127 + 7 = 134 = 100001102
Thus , 22810 using the IEEE 754 32-bit floating-point standard is
Most general purpose processors (including Intel and AMD processors) provide hardware support for double-precision floating-point numbers and operations
Mantissa /
22810 = 111001002 = 1.11001 × 27

## Slide 64: IEEE Floating Point Representation
Common finite representation: IEEE floating point
More precisely: ISO/IEEE 754 standard
Using 32 bits (type float in C):
1 bit: sign (0=>positive, 1=>negative)
8 bits: exponent + 127
23 bits: binary fraction of the form 1.ddddddddddddddddddddddd
Using 64 bits (type double in C):
1 bit: sign (0=>positive, 1=>negative)
11 bits: exponent + 1023
52 bits: binary fraction of the form 1.dddddddddddddddddddddddddddddddddddddddddddddddddddd
Mantissa /

## Slide 65: Example
Represent -5810 using the IEEE 754 floating-point standard
  First, convert the decimal number to binary
    5810 = 1110102 = 1.1101 × 25
  Next, fill in each field in the 32-bit number
    The sign bit is negative (1)
    The 8 exponent bits are (127 + 5) = 132 = 10000100(2)
    The remaining 23 bits are the fraction bits: 11010000...000(2)
  It is 0xC2680000 in the hexadecimal form
    Check this out with the result of the sample program in the slide# 3

## Slide 66: Double Precision Example
Represent -5810 using the IEEE 754 double precision
  First, convert the decimal number to binary
    5810 = 1110102 = 1.1101 × 25
  Next, fill in each field in the 64-bit number
    The sign bit is negative (1)
    The 11 exponent bits are (1023 + 5) = 1028 = 10000000100(2)
    The remaining 52 bits are the fraction bits: 11010000...000(2)
  It is 0xC04D000000000000 in the hexadecimal form

## Slide 67: Floating-Point Numbers: Special Cases
The IEEE 754 standard includes special cases for numbers that are difficult to represent, such as 0 because it lacks an implicit leading 1
Number | Sign | Exponent | Fraction
0 | X | 00000000 | 00000000000000000000000
∞ | 0 | 11111111 | 00000000000000000000000
- ∞ | 1 | 11111111 | 00000000000000000000000
NaN | X | 11111111 | non-zero
  NaN is used for numbers that don’t exist, such as √-1 or log(-5)

## Slide 68: Floating Point Example
Sign (1 bit):
1 => negative
Exponent (8 bits):
10000011B = 131
131 – 127 = 4
Fraction (23 bits):
1.10110110000000000000000B
1 +
(1*2-1)+(0*2-2)+(1*2-3)+(1*2-4)+(0*2-5)+(1*2-6)+(1*2-7)
= 1.7109375
Number:
-1.7109375 * 24 = -27.375
11000001110110110000000000000000
32-bit representation
Notes: https://www.youtube.com/watch?v=LXF-wcoeT0o

## Slide 69: Floating Point Example
263
2
131
2
65
2
32
2
16
2
8
2
4
2
2
2
1
2
0
1
1
1
0
0
0
0
0
1
263: 100000111
0.3 * 2 | 0.6 | 0
0.6 * 2 | 1.2 | 1
0.2 * 2 | 0.4 | 0
0.4 * 2 | 0.8 | 0
0.8 * 2 | 1.6 | 1
0.6 * 2 | 1.2 | 1
 |  | 0
 |  | 0
 |  | 1
 |  | 1
 |  | 0
0.3 : 01001100110011….
263.3
Stop when it gets 1.0
IEEE754 floating-point standard can’t represent some numbers exactly

## Slide 70: Floating Point Example
0100 0011 1000 0011 1010 0110 0110 0110
32-bit representation
263.3
100000111.0100110011…
2) Scientific notation:
1.000001110100110011… * 28
Mantissa
Sign (1 bit):
positive => 0
Exponent (8 bits):
127 + 8 = 135
135 = 10000111B
Fraction (23 bits):
00000111010011001100110
Notes: https://www.youtube.com/watch?v=8afbTaA-gOQ

## Slide 71: Binary Coded Decimal (BCD)
Since floating-point number systems can’t represent some numbers exactly such as 0.3, some application (calculators) use BCD (Binary coded decimal)
  BCD numbers encode each decimal digit using 4 bits with a range of 0 to 9
  BCD fixed-point notation examples
    1.7 = 0001 . 0111
    4.9 = 0100 . 1001
BCD is very common in electronic systems where a numeric value is to be displayed, especially, in systems consisting solely of digital logic (not containing a microprocessor) - Wiki
Decimal | BCD Digit
0 | 0000
1 | 0001
2 | 0010
3 | 0011
4 | 0100
5 | 0101
6 | 0110
7 | 0111
8 | 1000
9 | 1001
6.75 = 0110.01110101

## Slide 72: Converting Between Decimal and Binary Floating-Point Numbers
https://kyledewey.github.io/comp122-fall17/lecture/week_2/floating_point_interconversions.html

## Slide 73: Summary
The binary, hexadecimal, and octal number systems Finite representation of unsigned integers
Finite representation of signed integers Finite representation of rational numbers
Essential for proper understanding of
C primitive data types
Assembly language
Machine language

## Slide 74
Backup Slides

## Slide 75: Floating-Point Numbers: Rounding
Arithmetic results that fall outside of the available precision must round to a neighboring number
Rounding modes
  Round down
  Round up
  Round toward zero
  Round to nearest
Example
  Round 1.100101 (1.578125) so that it uses only 3 fraction bits
    Round down: 1.100
    Round up: 1.101
    Round toward zero: 1.100
    Round to nearest: 1.101
      1.625 is closer to 1.578125 than 1.5 is

## Slide 76: Floating-Point Addition with the Same Sign
Addition with floating-point numbers is not as simple as addition with 2’s complement numbers
The steps for adding floating-point numbers with the same sign are as follows
  Extract exponent and fraction bits
  Prepend leading 1 to form mantissa
  Compare exponents
  Shift smaller mantissa if necessary
  Add mantissas
  Normalize mantissa and adjust exponent if necessary
  Round result
  Assemble exponent and fraction back into floating-point format

## Slide 77: Floating-Point Addition Example
Add the following floating-point numbers:
1.5 + 3.25
1.5(10) = 1.1(2) x 20
3.25(10) = 11.01(2) = 1.101(2) x 21
1.1(10) = 0x3FC00000 in IEEE 754 single precision
3.25(10) = 0x40500000 in IEEE 754 single precision

## Slide 78: Floating-Point Addition Example
1. Extract exponent and fraction bits
For first number (N1): S = 0, E = 127, F = .1
For second number (N2): S = 0, E = 128, F = .101
2. Prepend leading 1 to form mantissa
N1: 1.1
N2: 1.101

## Slide 79: Floating-Point Addition Example
3. Compare exponents
127 – 128 = -1, so shift N1 right by 1 bit
4. Shift smaller mantissa if necessary
shift N1’s mantissa: 1.1 >> 1 = 0.11 (× 21)
5. Add mantissas
0.11 × 21
+ 1.101 × 21
10.011 × 21

## Slide 80: Floating-Point Addition Example
6. Normalize mantissa and adjust exponent if necessary
10.011 × 21 = 1.0011 × 22
7. Round result
No need (fits in 23 bits)
8. Assemble exponent and fraction back into floating-point format
S = 0, E = 2 + 127 = 129 = 100000012, F = 001100..
4.75(10) = 0x40980000 in the hexadecimal form